# IPv6 Configuration - Setting Up a Service VM as an IPv6 vRouter
OPNFV
February 09, 2016
[index::doc]
This section provides instructions to set up a service VM as an IPv6 vRouter using OPNFV Brahmaputra Release installers. The environment may be pure OpenStack option or Open Daylight L2-only option. The deployment model may be HA or non-HA. The infrastructure may be bare metal or virtual environment.
For complete instructions and documentations of setting up service VM as an IPv6 vRouter using ANY method, please refer to:
1. IPv6 Configuration Guide (HTML): http://artifacts.opnfv.org/ipv6/docs/setupservicevm/index.html
2. IPv6 User Guide (HTML): http://artifacts.opnfv.org/ipv6/docs/gapanalysis/index.html
# Pre-configuration Activities
[index:pre-configuration-activities][index:ipv6-configuration-setting-up-a-service-vm-as-an-ipv6-vrouter] The configuration will work in 2 environments:
1. OpenStack-only environment
2. OpenStack with Open Daylight L2-only environment
Depending on which installer will be used to deploy OPNFV, each environment may be deployed on bare metal or virtualized infrastructure. Each deployment may be HA or non-HA.
Refer to the previous installer configuration chapters, installations guide and release notes.
# Setup Manual in OpenStack-Only Environment
[index:setup-manual-in-openstack-only-environment] If you intend to set up a service VM as an IPv6 vRouter in OpenStack-only environment of OPNFV Brahmaputra Release, please NOTE that:
- Because the anti-spoofing rules of Security Group feature in OpenStack prevents a VM from forwarding packets, we need to disable Security Group feature in the OpenStack-only environment.
- The hostnames, IP addresses, and username are for exemplary purpose in instructions. Please change as needed to fit your environment.
- The instructions apply to both deployment model of single controller node and HA (High Availability) deployment model where multiple controller nodes are used.
## Install OPNFV and Preparation
[index:install-opnfv-and-preparation] OPNFV-NATIVE-INSTALL-1: To install OpenStack-only environment of OPNFV Brahmaputra Release:
Apex Installer:
\PYG{c}{\PYGZsh{} HA deployment in OpenStack\PYGZhy{}only environment}
sudo opnfv\PYGZhy{}deploy \PYGZhy{}d /etc/opnfv/os\PYGZhy{}nosdn\PYGZhy{}nofeature\PYGZhy{}ha.yaml

\PYG{c}{\PYGZsh{} Non\PYGZhy{}HA deployment in OpenStack\PYGZhy{}only environment}
\PYG{c}{\PYGZsh{} Non\PYGZhy{}HA deployment is currently not supported by Apex installer.}
Compass Installer:
\PYG{c}{\PYGZsh{} HA deployment in OpenStack\PYGZhy{}only environment}
\PYG{n+nb}{export }\PYG{n+nv}{ISO\PYGZus{}URL}\PYG{o}{=}file://\PYG{n+nv}{\PYGZdl{}BUILD\PYGZus{}DIRECTORY}/compass.iso
\PYG{n+nb}{export }\PYG{n+nv}{OS\PYGZus{}VERSION}\PYG{o}{=}\PYG{l+s+si}{\PYGZdl{}\PYGZob{}}\PYG{p}{\PYGZob{}COMPASS\PYGZus{}OS\PYGZus{}VERSION}\PYG{l+s+si}{\PYGZcb{}}\PYG{o}{\PYGZcb{}}
\PYG{n+nb}{export }\PYG{n+nv}{OPENSTACK\PYGZus{}VERSION}\PYG{o}{=}\PYG{l+s+si}{\PYGZdl{}\PYGZob{}}\PYG{p}{\PYGZob{}COMPASS\PYGZus{}OPENSTACK\PYGZus{}VERSION}\PYG{l+s+si}{\PYGZcb{}}\PYG{o}{\PYGZcb{}}
\PYG{n+nb}{export }\PYG{n+nv}{CONFDIR}\PYG{o}{=}\PYG{n+nv}{\PYGZdl{}WORKSPACE}/deploy/conf/vm\PYGZus{}environment
sudo ./deploy.sh \PYGZhy{}\PYGZhy{}dha \PYG{n+nv}{\PYGZdl{}CONFDIR}/os\PYGZhy{}nosdn\PYGZhy{}nofeature\PYGZhy{}ha.yml \PYG{l+s+se}{\PYGZbs{}}
\PYGZhy{}\PYGZhy{}network \PYG{n+nv}{\PYGZdl{}CONFDIR}/\PYG{n+nv}{\PYGZdl{}NODE\PYGZus{}NAME}/network.yml

\PYG{c}{\PYGZsh{} Non\PYGZhy{}HA deployment in OpenStack\PYGZhy{}only environment}
\PYG{c}{\PYGZsh{} Non\PYGZhy{}HA deployment is currently not supported by Compass installer}
Fuel Installer:
\PYG{c}{\PYGZsh{} HA deployment in OpenStack\PYGZhy{}only environment}
sudo ./deploy.sh \PYGZhy{}s os\PYGZhy{}nosdn\PYGZhy{}nofeature\PYGZhy{}ha

\PYG{c}{\PYGZsh{} Non\PYGZhy{}HA deployment in OpenStack\PYGZhy{}only environment}
sudo ./deploy.sh \PYGZhy{}s os\PYGZhy{}nosdn\PYGZhy{}nofeature\PYGZhy{}noha
Joid Installer:
\PYG{c}{\PYGZsh{} HA deployment in OpenStack\PYGZhy{}only environment}
sudo ./deploy.sh \PYGZhy{}o liberty \PYGZhy{}s nosdn \PYGZhy{}t ha

\PYG{c}{\PYGZsh{} Non\PYGZhy{}HA deployment in OpenStack\PYGZhy{}only environment}
sudo ./deploy.sh \PYGZhy{}o liberty \PYGZhy{}s nosdn \PYGZhy{}t noha
Please NOTE that you need to refer to installer’s documentation for other necessary parameters applicable to your deployment.
OPNFV-NATIVE-INSTALL-2: Clone the following GitHub repository to get the configuration and metadata files
git clone https://github.com/sridhargaddam/opnfv\PYGZus{}os\PYGZus{}ipv6\PYGZus{}poc.git \PYG{l+s+se}{\PYGZbs{}}
/opt/stack/opnfv\PYGZus{}os\PYGZus{}ipv6\PYGZus{}poc
## Disable Security Groups in OpenStack ML2 Setup
[index:disable-security-groups-in-openstack-ml2-setup] OPNFV-NATIVE-SEC-1: Change the settings in as follows
\PYG{c}{\PYGZsh{} /etc/neutron/plugins/ml2/ml2\PYGZus{}conf.ini}
\PYG{o}{[}securitygroup\PYG{o}{]}
\PYG{n+nv}{extension\PYGZus{}drivers} \PYG{o}{=} port\PYGZus{}security
\PYG{n+nv}{enable\PYGZus{}security\PYGZus{}group} \PYG{o}{=} False
\PYG{n+nv}{firewall\PYGZus{}driver} \PYG{o}{=} neutron.agent.firewall.NoopFirewallDriver
OPNFV-NATIVE-SEC-2: Change the settings in as follows
\PYG{c}{\PYGZsh{} /etc/nova/nova.conf}
\PYG{o}{[}DEFAULT\PYG{o}{]}
\PYG{n+nv}{security\PYGZus{}group\PYGZus{}api} \PYG{o}{=} nova
\PYG{n+nv}{firewall\PYGZus{}driver} \PYG{o}{=} nova.virt.firewall.NoopFirewallDriver
OPNFV-NATIVE-SEC-3: After updating the settings, you will have to restart the and services.
Please note that the commands of restarting and would vary depending on the installer. Please refer to relevant documentation of specific installers
## Set Up Service VM as IPv6 vRouter
[index:set-up-service-vm-as-ipv6-vrouter] OPNFV-NATIVE-SETUP-1: Now we assume that OpenStack multi-node setup is up and running. We have to source the tenant credentials in this step. Please NOTE that the method of sourcing tenant credentials may vary depending on installers. For example:
Apex installer:
\PYG{c}{\PYGZsh{} source the tenant credentials using Apex installer of OPNFV}
\PYG{c}{\PYGZsh{} you need to copy the file /home/stack/overcloudrc from the installer VM called \PYGZdq{}instack\PYGZdq{}}
\PYG{c}{\PYGZsh{} to a location in controller node, for example, in the directory /opt}
\PYG{n+nb}{source} /opt/overcloudrc
Compass installer:
\PYG{c}{\PYGZsh{} source the tenant credentials using Compass installer of OPNFV}
\PYG{n+nb}{source} /opt/admin\PYGZhy{}openrc.sh
Joid installer:
\PYG{c}{\PYGZsh{} source the tenant credentials using Joid installer of OPNFV}
\PYG{n+nb}{source} \PYG{n+nv}{\PYGZdl{}HOME}/joid\PYGZus{}config/admin\PYGZhy{}openrc
devstack:
\PYG{c}{\PYGZsh{} source the tenant credentials in devstack}
\PYG{n+nb}{source }openrc admin demo
Please refer to relevant documentation of installers if you encounter any issue.
OPNFV-NATIVE-SETUP-2: Download image which would be used for
wget https://download.fedoraproject.org/pub/fedora/linux/releases/22/Cloud/x86\PYGZus{}64/\PYG{l+s+se}{\PYGZbs{}}
Images/Fedora\PYGZhy{}Cloud\PYGZhy{}Base\PYGZhy{}22\PYGZhy{}20150521.x86\PYGZus{}64.qcow2
OPNFV-NATIVE-SETUP-3: Import Fedora22 image to
glance image\PYGZhy{}create \PYGZhy{}\PYGZhy{}name \PYG{l+s+s1}{\PYGZsq{}Fedora22\PYGZsq{}} \PYGZhy{}\PYGZhy{}disk\PYGZhy{}format qcow2 \PYGZhy{}\PYGZhy{}container\PYGZhy{}format bare \PYG{l+s+se}{\PYGZbs{}}
\PYGZhy{}\PYGZhy{}file ./Fedora\PYGZhy{}Cloud\PYGZhy{}Base\PYGZhy{}22\PYGZhy{}20150521.x86\PYGZus{}64.qcow2
OPNFV-NATIVE-SETUP-4: This step is Informational. OPNFV Installer has taken care of this step during deployment. You may refer to this step only if there is any issue, or if you are using other installers.
We have to move the physical interface (i.e. the public network interface) to , including moving the public IP address and setting up default route. Please refer to and in our more complete instruction.
OPNFV-NATIVE-SETUP-5: Create Neutron routers and which need to provide external connectivity.
neutron router\PYGZhy{}create ipv4\PYGZhy{}router
neutron router\PYGZhy{}create ipv6\PYGZhy{}router
OPNFV-NATIVE-SETUP-6: Create an external network/subnet using the appropriate values based on the data-center physical network setup.
Please NOTE that you may only need to create the subnet of because OPNFV installers should have created an external network during installation. You must use the same name of external network that installer creates when you create the subnet. For example:
- Apex installer:
- Compass installer:
- Fuel installer:
- Joid installer:
Please refer to the documentation of installers if there is any issue
\PYG{c}{\PYGZsh{} This is needed only if installer does not create an external work}
\PYG{c}{\PYGZsh{} Otherwise, skip this command \PYGZdq{}net\PYGZhy{}create\PYGZdq{}}
neutron net\PYGZhy{}create \PYGZhy{}\PYGZhy{}router:external ext\PYGZhy{}net

\PYG{c}{\PYGZsh{} Note that the name \PYGZdq{}ext\PYGZhy{}net\PYGZdq{} may work for some installers such as Compass and Joid}
\PYG{c}{\PYGZsh{} Change the name \PYGZdq{}ext\PYGZhy{}net\PYGZdq{} to match the name of external network that an installer creates}
neutron subnet\PYGZhy{}create \PYGZhy{}\PYGZhy{}disable\PYGZhy{}dhcp \PYGZhy{}\PYGZhy{}allocation\PYGZhy{}pool \PYG{n+nv}{start}\PYG{o}{=}198.59.156.251,\PYG{l+s+se}{\PYGZbs{}}
\PYG{n+nv}{end}\PYG{o}{=}198.59.156.254 \PYGZhy{}\PYGZhy{}gateway 198.59.156.1 ext\PYGZhy{}net 198.59.156.0/24
OPNFV-NATIVE-SETUP-7: Create Neutron networks and with port_security disabled
neutron net\PYGZhy{}create \PYGZhy{}\PYGZhy{}port\PYGZus{}security\PYGZus{}enabled\PYG{o}{=}False ipv4\PYGZhy{}int\PYGZhy{}network1
neutron net\PYGZhy{}create \PYGZhy{}\PYGZhy{}port\PYGZus{}security\PYGZus{}enabled\PYG{o}{=}False ipv6\PYGZhy{}int\PYGZhy{}network2
OPNFV-NATIVE-SETUP-8: Create IPv4 subnet in the internal network , and associate it to .
neutron subnet\PYGZhy{}create \PYGZhy{}\PYGZhy{}name ipv4\PYGZhy{}int\PYGZhy{}subnet1 \PYGZhy{}\PYGZhy{}dns\PYGZhy{}nameserver 8.8.8.8 \PYG{l+s+se}{\PYGZbs{}}
ipv4\PYGZhy{}int\PYGZhy{}network1 20.0.0.0/24

neutron router\PYGZhy{}interface\PYGZhy{}add ipv4\PYGZhy{}router ipv4\PYGZhy{}int\PYGZhy{}subnet1
OPNFV-NATIVE-SETUP-9: Associate the to the Neutron routers and .
\PYG{c}{\PYGZsh{} Note that the name \PYGZdq{}ext\PYGZhy{}net\PYGZdq{} may work for some installers such as Compass and Joid}
\PYG{c}{\PYGZsh{} Change the name \PYGZdq{}ext\PYGZhy{}net\PYGZdq{} to match the name of external network that an installer creates}
neutron router\PYGZhy{}gateway\PYGZhy{}set ipv4\PYGZhy{}router ext\PYGZhy{}net
neutron router\PYGZhy{}gateway\PYGZhy{}set ipv6\PYGZhy{}router ext\PYGZhy{}net
OPNFV-NATIVE-SETUP-10: Create two subnets, one IPv4 subnet and one IPv6 subnet in , and associate both subnets to
neutron subnet\PYGZhy{}create \PYGZhy{}\PYGZhy{}name ipv4\PYGZhy{}int\PYGZhy{}subnet2 \PYGZhy{}\PYGZhy{}dns\PYGZhy{}nameserver 8.8.8.8 \PYG{l+s+se}{\PYGZbs{}}
ipv6\PYGZhy{}int\PYGZhy{}network2 10.0.0.0/24

neutron subnet\PYGZhy{}create \PYGZhy{}\PYGZhy{}name ipv6\PYGZhy{}int\PYGZhy{}subnet2 \PYGZhy{}\PYGZhy{}ip\PYGZhy{}version \PYG{l+m}{6} \PYGZhy{}\PYGZhy{}ipv6\PYGZhy{}ra\PYGZhy{}mode slaac \PYG{l+s+se}{\PYGZbs{}}
\PYGZhy{}\PYGZhy{}ipv6\PYGZhy{}address\PYGZhy{}mode slaac ipv6\PYGZhy{}int\PYGZhy{}network2 2001:db8:0:1::/64

neutron router\PYGZhy{}interface\PYGZhy{}add ipv6\PYGZhy{}router ipv4\PYGZhy{}int\PYGZhy{}subnet2
neutron router\PYGZhy{}interface\PYGZhy{}add ipv6\PYGZhy{}router ipv6\PYGZhy{}int\PYGZhy{}subnet2
OPNFV-NATIVE-SETUP-11: Create a keypair
nova keypair\PYGZhy{}add vRouterKey \PYGZgt{} \PYGZti{}/vRouterKey
OPNFV-NATIVE-SETUP-12: Create ports for vRouter (with some specific MAC address - basically for automation - to know the IPv6 addresses that would be assigned to the port).
neutron port\PYGZhy{}create \PYGZhy{}\PYGZhy{}name eth0\PYGZhy{}vRouter \PYGZhy{}\PYGZhy{}mac\PYGZhy{}address fa:16:3e:11:11:11 ipv6\PYGZhy{}int\PYGZhy{}network2
neutron port\PYGZhy{}create \PYGZhy{}\PYGZhy{}name eth1\PYGZhy{}vRouter \PYGZhy{}\PYGZhy{}mac\PYGZhy{}address fa:16:3e:22:22:22 ipv4\PYGZhy{}int\PYGZhy{}network1
OPNFV-NATIVE-SETUP-13: Create ports for VM1 and VM2.
neutron port\PYGZhy{}create \PYGZhy{}\PYGZhy{}name eth0\PYGZhy{}VM1 \PYGZhy{}\PYGZhy{}mac\PYGZhy{}address fa:16:3e:33:33:33 ipv4\PYGZhy{}int\PYGZhy{}network1
neutron port\PYGZhy{}create \PYGZhy{}\PYGZhy{}name eth0\PYGZhy{}VM2 \PYGZhy{}\PYGZhy{}mac\PYGZhy{}address fa:16:3e:44:44:44 ipv4\PYGZhy{}int\PYGZhy{}network1
OPNFV-NATIVE-SETUP-14: Update with routing information to subnet
neutron router\PYGZhy{}update ipv6\PYGZhy{}router \PYGZhy{}\PYGZhy{}routes \PYG{n+nb}{type}\PYG{o}{=}dict \PYG{n+nv}{list}\PYG{o}{=}\PYG{n+nb}{true} \PYG{l+s+se}{\PYGZbs{}}
\PYG{n+nv}{destination}\PYG{o}{=}2001:db8:0:2::/64,nexthop\PYG{o}{=}2001:db8:0:1:f816:3eff:fe11:1111
OPNFV-NATIVE-SETUP-15: Boot Service VM (), VM1 and VM2
nova boot \PYGZhy{}\PYGZhy{}image Fedora22 \PYGZhy{}\PYGZhy{}flavor m1.small \PYG{l+s+se}{\PYGZbs{}}
\PYGZhy{}\PYGZhy{}user\PYGZhy{}data /opt/stack/opnfv\PYGZus{}os\PYGZus{}ipv6\PYGZus{}poc/metadata.txt \PYG{l+s+se}{\PYGZbs{}}
\PYGZhy{}\PYGZhy{}availability\PYGZhy{}zone nova:opnfv\PYGZhy{}os\PYGZhy{}compute \PYG{l+s+se}{\PYGZbs{}}
\PYGZhy{}\PYGZhy{}nic port\PYGZhy{}id\PYG{o}{=}\PYG{k}{\PYGZdl{}(}neutron port\PYGZhy{}list \PYG{p}{\textbar{}} grep \PYGZhy{}w eth0\PYGZhy{}vRouter \PYG{p}{\textbar{}} awk \PYG{l+s+s1}{\PYGZsq{}\PYGZob{}print \PYGZdl{}2\PYGZcb{}\PYGZsq{}}\PYG{k}{)} \PYG{l+s+se}{\PYGZbs{}}
\PYGZhy{}\PYGZhy{}nic port\PYGZhy{}id\PYG{o}{=}\PYG{k}{\PYGZdl{}(}neutron port\PYGZhy{}list \PYG{p}{\textbar{}} grep \PYGZhy{}w eth1\PYGZhy{}vRouter \PYG{p}{\textbar{}} awk \PYG{l+s+s1}{\PYGZsq{}\PYGZob{}print \PYGZdl{}2\PYGZcb{}\PYGZsq{}}\PYG{k}{)} \PYG{l+s+se}{\PYGZbs{}}
\PYGZhy{}\PYGZhy{}key\PYGZhy{}name vRouterKey vRouter

nova list

\PYG{c}{\PYGZsh{} Please wait for some 10 to 15 minutes so that necessary packages (like radvd)}
\PYG{c}{\PYGZsh{} are installed and vRouter is up.}
nova console\PYGZhy{}log vRouter

nova boot \PYGZhy{}\PYGZhy{}image cirros\PYGZhy{}0.3.4\PYGZhy{}x86\PYGZus{}64\PYGZhy{}uec \PYGZhy{}\PYGZhy{}flavor m1.tiny \PYG{l+s+se}{\PYGZbs{}}
\PYGZhy{}\PYGZhy{}user\PYGZhy{}data /opt/stack/opnfv\PYGZus{}os\PYGZus{}ipv6\PYGZus{}poc/set\PYGZus{}mtu.sh \PYG{l+s+se}{\PYGZbs{}}
\PYGZhy{}\PYGZhy{}availability\PYGZhy{}zone nova:opnfv\PYGZhy{}os\PYGZhy{}controller \PYG{l+s+se}{\PYGZbs{}}
\PYGZhy{}\PYGZhy{}nic port\PYGZhy{}id\PYG{o}{=}\PYG{k}{\PYGZdl{}(}neutron port\PYGZhy{}list \PYG{p}{\textbar{}} grep \PYGZhy{}w eth0\PYGZhy{}VM1 \PYG{p}{\textbar{}} awk \PYG{l+s+s1}{\PYGZsq{}\PYGZob{}print \PYGZdl{}2\PYGZcb{}\PYGZsq{}}\PYG{k}{)} \PYG{l+s+se}{\PYGZbs{}}
\PYGZhy{}\PYGZhy{}key\PYGZhy{}name vRouterKey VM1

nova boot \PYGZhy{}\PYGZhy{}image cirros\PYGZhy{}0.3.4\PYGZhy{}x86\PYGZus{}64\PYGZhy{}uec \PYGZhy{}\PYGZhy{}flavor m1.tiny
\PYGZhy{}\PYGZhy{}user\PYGZhy{}data /opt/stack/opnfv\PYGZus{}os\PYGZus{}ipv6\PYGZus{}poc/set\PYGZus{}mtu.sh \PYG{l+s+se}{\PYGZbs{}}
\PYGZhy{}\PYGZhy{}availability\PYGZhy{}zone nova:opnfv\PYGZhy{}os\PYGZhy{}compute \PYG{l+s+se}{\PYGZbs{}}
\PYGZhy{}\PYGZhy{}nic port\PYGZhy{}id\PYG{o}{=}\PYG{k}{\PYGZdl{}(}neutron port\PYGZhy{}list \PYG{p}{\textbar{}} grep \PYGZhy{}w eth0\PYGZhy{}VM2 \PYG{p}{\textbar{}} awk \PYG{l+s+s1}{\PYGZsq{}\PYGZob{}print \PYGZdl{}2\PYGZcb{}\PYGZsq{}}\PYG{k}{)} \PYG{l+s+se}{\PYGZbs{}}
\PYGZhy{}\PYGZhy{}key\PYGZhy{}name vRouterKey VM2

nova list \PYG{c}{\PYGZsh{} Verify that all the VMs are in ACTIVE state.}
OPNFV-NATIVE-SETUP-16: If all goes well, the IPv6 addresses assigned to the VMs would be as shown as follows:
\PYG{c}{\PYGZsh{} vRouter eth0 interface would have the following IPv6 address:}
\PYG{c}{\PYGZsh{} 2001:db8:0:1:f816:3eff:fe11:1111/64}
\PYG{c}{\PYGZsh{} vRouter eth1 interface would have the following IPv6 address:}
\PYG{c}{\PYGZsh{} 2001:db8:0:2::1/64}
\PYG{c}{\PYGZsh{} VM1 would have the following IPv6 address:}
\PYG{c}{\PYGZsh{} 2001:db8:0:2:f816:3eff:fe33:3333/64}
\PYG{c}{\PYGZsh{} VM2 would have the following IPv6 address:}
\PYG{c}{\PYGZsh{} 2001:db8:0:2:f816:3eff:fe44:4444/64}
OPNFV-NATIVE-SETUP-17: Now we can to VMs. You can execute the following command.
\PYG{c}{\PYGZsh{} 1. Create a floatingip and associate it with VM1, VM2 and vRouter (to the port id that is passed).}
\PYG{c}{\PYGZsh{} Note that the name \PYGZdq{}ext\PYGZhy{}net\PYGZdq{} may work for some installers such as Compass and Joid}
\PYG{c}{\PYGZsh{} Change the name \PYGZdq{}ext\PYGZhy{}net\PYGZdq{} to match the name of external network that an installer creates}
neutron floatingip\PYGZhy{}create \PYGZhy{}\PYGZhy{}port\PYGZhy{}id \PYG{k}{\PYGZdl{}(}neutron port\PYGZhy{}list \PYG{p}{\textbar{}} grep \PYGZhy{}w eth0\PYGZhy{}VM1 \PYG{p}{\textbar{}} \PYG{l+s+se}{\PYGZbs{}}
awk \PYG{l+s+s1}{\PYGZsq{}\PYGZob{}print \PYGZdl{}2\PYGZcb{}\PYGZsq{}}\PYG{k}{)} ext\PYGZhy{}net
neutron floatingip\PYGZhy{}create \PYGZhy{}\PYGZhy{}port\PYGZhy{}id \PYG{k}{\PYGZdl{}(}neutron port\PYGZhy{}list \PYG{p}{\textbar{}} grep \PYGZhy{}w eth0\PYGZhy{}VM2 \PYG{p}{\textbar{}} \PYG{l+s+se}{\PYGZbs{}}
awk \PYG{l+s+s1}{\PYGZsq{}\PYGZob{}print \PYGZdl{}2\PYGZcb{}\PYGZsq{}}\PYG{k}{)} ext\PYGZhy{}net
neutron floatingip\PYGZhy{}create \PYGZhy{}\PYGZhy{}port\PYGZhy{}id \PYG{k}{\PYGZdl{}(}neutron port\PYGZhy{}list \PYG{p}{\textbar{}} grep \PYGZhy{}w eth1\PYGZhy{}vRouter \PYG{p}{\textbar{}} \PYG{l+s+se}{\PYGZbs{}}
awk \PYG{l+s+s1}{\PYGZsq{}\PYGZob{}print \PYGZdl{}2\PYGZcb{}\PYGZsq{}}\PYG{k}{)} ext\PYGZhy{}net

\PYG{c}{\PYGZsh{} 2. To know / display the floatingip associated with VM1, VM2 and vRouter.}
neutron floatingip\PYGZhy{}list \PYGZhy{}F floating\PYGZus{}ip\PYGZus{}address \PYGZhy{}F port\PYGZus{}id \PYG{p}{\textbar{}} grep \PYG{k}{\PYGZdl{}(}neutron port\PYGZhy{}list \PYG{p}{\textbar{}} \PYG{l+s+se}{\PYGZbs{}}
grep \PYGZhy{}w eth0\PYGZhy{}VM1 \PYG{p}{\textbar{}} awk \PYG{l+s+s1}{\PYGZsq{}\PYGZob{}print \PYGZdl{}2\PYGZcb{}\PYGZsq{}}\PYG{k}{)} \PYG{p}{\textbar{}} awk \PYG{l+s+s1}{\PYGZsq{}\PYGZob{}print \PYGZdl{}2\PYGZcb{}\PYGZsq{}}
neutron floatingip\PYGZhy{}list \PYGZhy{}F floating\PYGZus{}ip\PYGZus{}address \PYGZhy{}F port\PYGZus{}id \PYG{p}{\textbar{}} grep \PYG{k}{\PYGZdl{}(}neutron port\PYGZhy{}list \PYG{p}{\textbar{}} \PYG{l+s+se}{\PYGZbs{}}
grep \PYGZhy{}w eth0\PYGZhy{}VM2 \PYG{p}{\textbar{}} awk \PYG{l+s+s1}{\PYGZsq{}\PYGZob{}print \PYGZdl{}2\PYGZcb{}\PYGZsq{}}\PYG{k}{)} \PYG{p}{\textbar{}} awk \PYG{l+s+s1}{\PYGZsq{}\PYGZob{}print \PYGZdl{}2\PYGZcb{}\PYGZsq{}}
neutron floatingip\PYGZhy{}list \PYGZhy{}F floating\PYGZus{}ip\PYGZus{}address \PYGZhy{}F port\PYGZus{}id \PYG{p}{\textbar{}} grep \PYG{k}{\PYGZdl{}(}neutron port\PYGZhy{}list \PYG{p}{\textbar{}} \PYG{l+s+se}{\PYGZbs{}}
grep \PYGZhy{}w eth1\PYGZhy{}vRouter \PYG{p}{\textbar{}} awk \PYG{l+s+s1}{\PYGZsq{}\PYGZob{}print \PYGZdl{}2\PYGZcb{}\PYGZsq{}}\PYG{k}{)} \PYG{p}{\textbar{}} awk \PYG{l+s+s1}{\PYGZsq{}\PYGZob{}print \PYGZdl{}2\PYGZcb{}\PYGZsq{}}

\PYG{c}{\PYGZsh{} 3. To ssh to the vRouter, VM1 and VM2, user can execute the following command.}
ssh \PYGZhy{}i \PYGZti{}/vRouterKey fedora@\PYGZlt{}floating\PYGZhy{}ip\PYGZhy{}of\PYGZhy{}vRouter\PYGZgt{}
ssh \PYGZhy{}i \PYGZti{}/vRouterKey cirros@\PYGZlt{}floating\PYGZhy{}ip\PYGZhy{}of\PYGZhy{}VM1\PYGZgt{}
ssh \PYGZhy{}i \PYGZti{}/vRouterKey cirros@\PYGZlt{}floating\PYGZhy{}ip\PYGZhy{}of\PYGZhy{}VM2\PYGZgt{}
# Setup Manual in OpenStack with Open Daylight L2-Only Environment
[index:setup-manual-in-openstack-with-open-daylight-l2-only-environment] If you intend to set up a service VM as an IPv6 vRouter in an environment of OpenStack and Open Daylight L2-only of OPNFV Brahmaputra Release, please NOTE that:
- The hostnames, IP addresses, and username are for exemplary purpose in instructions. Please change as needed to fit your environment.
- The instructions apply to both deployment model of single controller node and HA (High Availability) deployment model where multiple controller nodes are used.
- However, in case of HA, when is created in step SETUP-SVM-11, it could be created in any of the controller node. Thus you need to identify in which controller node is created in order to manually spawn daemon inside the namespace in steps SETUP-SVM-24 through SETUP-SVM-30.
## Install OPNFV and Preparation
[index:id1] OPNFV-INSTALL-1: To install OpenStack with Open Daylight L2-only environment of OPNFV Brahmaputra Release:
Apex Installer:
\PYG{c}{\PYGZsh{} HA deployment in OpenStack with Open Daylight L2\PYGZhy{}only environment}
sudo opnfv\PYGZhy{}deploy \PYGZhy{}d /etc/opnfv/os\PYGZhy{}odl\PYGZus{}l2\PYGZhy{}nofeature\PYGZhy{}ha.yaml

\PYG{c}{\PYGZsh{} Non\PYGZhy{}HA deployment in OpenStack with Open Daylight L2\PYGZhy{}only environment}
\PYG{c}{\PYGZsh{} Non\PYGZhy{}HA deployment is currently not supported by Apex installer.}
Compass Installer:
\PYG{c}{\PYGZsh{} HA deployment in OpenStack with Open Daylight L2\PYGZhy{}only environment}
\PYG{n+nb}{export }\PYG{n+nv}{ISO\PYGZus{}URL}\PYG{o}{=}file://\PYG{n+nv}{\PYGZdl{}BUILD\PYGZus{}DIRECTORY}/compass.iso
\PYG{n+nb}{export }\PYG{n+nv}{OS\PYGZus{}VERSION}\PYG{o}{=}\PYG{l+s+si}{\PYGZdl{}\PYGZob{}}\PYG{p}{\PYGZob{}COMPASS\PYGZus{}OS\PYGZus{}VERSION}\PYG{l+s+si}{\PYGZcb{}}\PYG{o}{\PYGZcb{}}
\PYG{n+nb}{export }\PYG{n+nv}{OPENSTACK\PYGZus{}VERSION}\PYG{o}{=}\PYG{l+s+si}{\PYGZdl{}\PYGZob{}}\PYG{p}{\PYGZob{}COMPASS\PYGZus{}OPENSTACK\PYGZus{}VERSION}\PYG{l+s+si}{\PYGZcb{}}\PYG{o}{\PYGZcb{}}
\PYG{n+nb}{export }\PYG{n+nv}{CONFDIR}\PYG{o}{=}\PYG{n+nv}{\PYGZdl{}WORKSPACE}/deploy/conf/vm\PYGZus{}environment
sudo ./deploy.sh \PYGZhy{}\PYGZhy{}dha \PYG{n+nv}{\PYGZdl{}CONFDIR}/os\PYGZhy{}odl\PYGZus{}l2\PYGZhy{}nofeature\PYGZhy{}ha.yml \PYG{l+s+se}{\PYGZbs{}}
\PYGZhy{}\PYGZhy{}network \PYG{n+nv}{\PYGZdl{}CONFDIR}/\PYG{n+nv}{\PYGZdl{}NODE\PYGZus{}NAME}/network.yml

\PYG{c}{\PYGZsh{} Non\PYGZhy{}HA deployment in OpenStack with Open Daylight L2\PYGZhy{}only environment}
\PYG{c}{\PYGZsh{} Non\PYGZhy{}HA deployment is currently not supported by Compass installer}
Fuel Installer:
\PYG{c}{\PYGZsh{} HA deployment in OpenStack with Open Daylight L2\PYGZhy{}only environment}
sudo ./deploy.sh \PYGZhy{}s os\PYGZhy{}odl\PYGZus{}l2\PYGZhy{}nofeature\PYGZhy{}ha

\PYG{c}{\PYGZsh{} Non\PYGZhy{}HA deployment in OpenStack with Open Daylight L2\PYGZhy{}only environment}
sudo ./deploy.sh \PYGZhy{}s os\PYGZhy{}odl\PYGZus{}l2\PYGZhy{}nofeature\PYGZhy{}noha
Please NOTE that:
- Currently only , and installer support this environment.
- You need to refer to installer’s documentation for other necessary parameters applicable to your deployment.
OPNFV-INSTALL-2: Clone the following GitHub repository to get the configuration and metadata files
git clone https://github.com/sridhargaddam/opnfv\PYGZus{}os\PYGZus{}ipv6\PYGZus{}poc.git \PYG{l+s+se}{\PYGZbs{}}
/opt/stack/opnfv\PYGZus{}os\PYGZus{}ipv6\PYGZus{}poc
## Disable Security Groups in OpenStack ML2 Setup
[index:id2] Please NOTE that although Security Groups feature has been disabled automatically through configuration file by some installers such as , it is very likely that other installers such as , , or will enable Security Groups feature after installation.
Please make sure that Security Groups are disabled in the setup
OPNFV-SEC-1: Change the settings in as follows
\PYG{c}{\PYGZsh{} /etc/neutron/plugins/ml2/ml2\PYGZus{}conf.ini}
\PYG{o}{[}securitygroup\PYG{o}{]}
\PYG{n+nv}{enable\PYGZus{}security\PYGZus{}group} \PYG{o}{=} False
\PYG{n+nv}{firewall\PYGZus{}driver} \PYG{o}{=} neutron.agent.firewall.NoopFirewallDriver
OPNFV-SEC-2: Change the settings in as follows
\PYG{c}{\PYGZsh{} /etc/nova/nova.conf}
\PYG{o}{[}DEFAULT\PYG{o}{]}
\PYG{n+nv}{security\PYGZus{}group\PYGZus{}api} \PYG{o}{=} nova
\PYG{n+nv}{firewall\PYGZus{}driver} \PYG{o}{=} nova.virt.firewall.NoopFirewallDriver
OPNFV-SEC-3: After updating the settings, you will have to restart the and services.
Please note that the commands of restarting and would vary depending on the installer. Please refer to relevant documentation of specific installers
## Source the Credentials in OpenStack Controller Node
[index:source-the-credentials-in-openstack-controller-node] SETUP-SVM-1: Login in OpenStack Controller Node. Start a new terminal, and change directory to where OpenStack is installed.
SETUP-SVM-2: We have to source the tenant credentials in this step. Please NOTE that the method of sourcing tenant credentials may vary depending on installers. For example:
Apex installer:
\PYG{c}{\PYGZsh{} source the tenant credentials using Apex installer of OPNFV}
\PYG{c}{\PYGZsh{} you need to copy the file /home/stack/overcloudrc from the installer VM called \PYGZdq{}instack\PYGZdq{}}
\PYG{c}{\PYGZsh{} to a location in controller node, for example, in the directory /opt}
\PYG{n+nb}{source} /opt/overcloudrc
Compass installer:
\PYG{c}{\PYGZsh{} source the tenant credentials using Compass installer of OPNFV}
\PYG{n+nb}{source} /opt/admin\PYGZhy{}openrc.sh
Joid installer:
\PYG{c}{\PYGZsh{} source the tenant credentials using Joid installer of OPNFV}
\PYG{n+nb}{source} \PYG{n+nv}{\PYGZdl{}HOME}/joid\PYGZus{}config/admin\PYGZhy{}openrc
devstack:
\PYG{c}{\PYGZsh{} source the tenant credentials in devstack}
\PYG{n+nb}{source }openrc admin demo
Please refer to relevant documentation of installers if you encounter any issue.
## Informational Note: Move Public Network from Physical Network Interface to br-ex
[index:informational-note-move-public-network-from-physical-network-interface-to-br-ex] SETUP-SVM-3: Move the physical interface (i.e. the public network interface) to
SETUP-SVM-4: Verify setup of
Those 2 steps are Informational. OPNFV Installer has taken care of those 2 steps during deployment. You may refer to this step only if there is any issue, or if you are using other installers.
We have to move the physical interface (i.e. the public network interface) to , including moving the public IP address and setting up default route. Please refer to and in our more complete instruction.
## Create IPv4 Subnet and Router with External Connectivity
[index:create-ipv4-subnet-and-router-with-external-connectivity] SETUP-SVM-5: Create a Neutron router which needs to provide external connectivity.
neutron router\PYGZhy{}create ipv4\PYGZhy{}router
SETUP-SVM-6: Create an external network/subnet using the appropriate values based on the data-center physical network setup.
Please NOTE that you may only need to create the subnet of because OPNFV installers should have created an external network during installation. You must use the same name of external network that installer creates when you create the subnet. For example:
- Apex installer:
- Compass installer:
- Fuel installer:
- Joid installer:
Please refer to the documentation of installers if there is any issue
\PYG{c}{\PYGZsh{} This is needed only if installer does not create an external work}
\PYG{c}{\PYGZsh{} Otherwise, skip this command \PYGZdq{}net\PYGZhy{}create\PYGZdq{}}
neutron net\PYGZhy{}create \PYGZhy{}\PYGZhy{}router:external ext\PYGZhy{}net

\PYG{c}{\PYGZsh{} Note that the name \PYGZdq{}ext\PYGZhy{}net\PYGZdq{} may work for some installers such as Compass and Joid}
\PYG{c}{\PYGZsh{} Change the name \PYGZdq{}ext\PYGZhy{}net\PYGZdq{} to match the name of external network that an installer creates}
neutron subnet\PYGZhy{}create \PYGZhy{}\PYGZhy{}disable\PYGZhy{}dhcp \PYGZhy{}\PYGZhy{}allocation\PYGZhy{}pool \PYG{n+nv}{start}\PYG{o}{=}198.59.156.251,\PYG{l+s+se}{\PYGZbs{}}
\PYG{n+nv}{end}\PYG{o}{=}198.59.156.254 \PYGZhy{}\PYGZhy{}gateway 198.59.156.1 ext\PYGZhy{}net 198.59.156.0/24
Please note that the IP addresses in the command above are for exemplary purpose. Please replace the IP addresses of your actual network.
SETUP-SVM-7: Associate the to the Neutron router .
\PYG{c}{\PYGZsh{} Note that the name \PYGZdq{}ext\PYGZhy{}net\PYGZdq{} may work for some installers such as Compass and Joid}
\PYG{c}{\PYGZsh{} Change the name \PYGZdq{}ext\PYGZhy{}net\PYGZdq{} to match the name of external network that an installer creates}
neutron router\PYGZhy{}gateway\PYGZhy{}set ipv4\PYGZhy{}router ext\PYGZhy{}net
SETUP-SVM-8: Create an internal/tenant IPv4 network
neutron net\PYGZhy{}create ipv4\PYGZhy{}int\PYGZhy{}network1
SETUP-SVM-9: Create an IPv4 subnet in the internal network
neutron subnet\PYGZhy{}create \PYGZhy{}\PYGZhy{}name ipv4\PYGZhy{}int\PYGZhy{}subnet1 \PYGZhy{}\PYGZhy{}dns\PYGZhy{}nameserver 8.8.8.8 \PYG{l+s+se}{\PYGZbs{}}
ipv4\PYGZhy{}int\PYGZhy{}network1 20.0.0.0/24
SETUP-SVM-10: Associate the IPv4 internal subnet to the Neutron router .
neutron router\PYGZhy{}interface\PYGZhy{}add ipv4\PYGZhy{}router ipv4\PYGZhy{}int\PYGZhy{}subnet1
## Create IPv6 Subnet and Router with External Connectivity
[index:create-ipv6-subnet-and-router-with-external-connectivity] Now, let us create a second neutron router where we can “manually” spawn a daemon to simulate an external IPv6 router.
SETUP-SVM-11: Create a second Neutron router which needs to provide external connectivity
neutron router\PYGZhy{}create ipv6\PYGZhy{}router
SETUP-SVM-12: Associate the to the Neutron router
\PYG{c}{\PYGZsh{} Note that the name \PYGZdq{}ext\PYGZhy{}net\PYGZdq{} may work for some installers such as Compass and Joid}
\PYG{c}{\PYGZsh{} Change the name \PYGZdq{}ext\PYGZhy{}net\PYGZdq{} to match the name of external network that an installer creates}
neutron router\PYGZhy{}gateway\PYGZhy{}set ipv6\PYGZhy{}router ext\PYGZhy{}net
SETUP-SVM-13: Create a second internal/tenant IPv4 network
neutron net\PYGZhy{}create ipv4\PYGZhy{}int\PYGZhy{}network2
SETUP-SVM-14: Create an IPv4 subnet for the internal network
neutron subnet\PYGZhy{}create \PYGZhy{}\PYGZhy{}name ipv4\PYGZhy{}int\PYGZhy{}subnet2 \PYGZhy{}\PYGZhy{}dns\PYGZhy{}nameserver 8.8.8.8 \PYG{l+s+se}{\PYGZbs{}}
ipv4\PYGZhy{}int\PYGZhy{}network2 10.0.0.0/24
SETUP-SVM-15: Associate the IPv4 internal subnet to the Neutron router .
neutron router\PYGZhy{}interface\PYGZhy{}add ipv6\PYGZhy{}router ipv4\PYGZhy{}int\PYGZhy{}subnet2
## Prepare Image, Metadata and Keypair for Service VM
[index:prepare-image-metadata-and-keypair-for-service-vm] SETUP-SVM-16: Download image which would be used as
wget https://download.fedoraproject.org/pub/fedora/linux/releases/22/Cloud/x86\PYGZus{}64/\PYG{l+s+se}{\PYGZbs{}}
Images/Fedora\PYGZhy{}Cloud\PYGZhy{}Base\PYGZhy{}22\PYGZhy{}20150521.x86\PYGZus{}64.qcow2

glance image\PYGZhy{}create \PYGZhy{}\PYGZhy{}name \PYG{l+s+s1}{\PYGZsq{}Fedora22\PYGZsq{}} \PYGZhy{}\PYGZhy{}disk\PYGZhy{}format qcow2 \PYGZhy{}\PYGZhy{}container\PYGZhy{}format bare \PYG{l+s+se}{\PYGZbs{}}
\PYGZhy{}\PYGZhy{}file ./Fedora\PYGZhy{}Cloud\PYGZhy{}Base\PYGZhy{}22\PYGZhy{}20150521.x86\PYGZus{}64.qcow2
SETUP-SVM-17: Create a keypair
nova keypair\PYGZhy{}add vRouterKey \PYGZgt{} \PYGZti{}/vRouterKey
SETUP-SVM-18: Create ports for and both the VMs with some specific MAC addresses.
neutron port\PYGZhy{}create \PYGZhy{}\PYGZhy{}name eth0\PYGZhy{}vRouter \PYGZhy{}\PYGZhy{}mac\PYGZhy{}address fa:16:3e:11:11:11 ipv4\PYGZhy{}int\PYGZhy{}network2
neutron port\PYGZhy{}create \PYGZhy{}\PYGZhy{}name eth1\PYGZhy{}vRouter \PYGZhy{}\PYGZhy{}mac\PYGZhy{}address fa:16:3e:22:22:22 ipv4\PYGZhy{}int\PYGZhy{}network1
neutron port\PYGZhy{}create \PYGZhy{}\PYGZhy{}name eth0\PYGZhy{}VM1 \PYGZhy{}\PYGZhy{}mac\PYGZhy{}address fa:16:3e:33:33:33 ipv4\PYGZhy{}int\PYGZhy{}network1
neutron port\PYGZhy{}create \PYGZhy{}\PYGZhy{}name eth0\PYGZhy{}VM2 \PYGZhy{}\PYGZhy{}mac\PYGZhy{}address fa:16:3e:44:44:44 ipv4\PYGZhy{}int\PYGZhy{}network1
## Boot Service VM (vRouter) with eth0 on ipv4-int-network2 and eth1 on ipv4-int-network1
[index:boot-service-vm-vrouter-with-eth0-on-ipv4-int-network2-and-eth1-on-ipv4-int-network1] Let us boot the service VM () with interface on connecting to , and interface on connecting to .
SETUP-SVM-19: Boot the using image on the OpenStack Compute Node with hostname
nova boot \PYGZhy{}\PYGZhy{}image Fedora22 \PYGZhy{}\PYGZhy{}flavor m1.small \PYG{l+s+se}{\PYGZbs{}}
\PYGZhy{}\PYGZhy{}user\PYGZhy{}data /opt/stack/opnfv\PYGZus{}os\PYGZus{}ipv6\PYGZus{}poc/metadata.txt \PYG{l+s+se}{\PYGZbs{}}
\PYGZhy{}\PYGZhy{}availability\PYGZhy{}zone nova:opnfv\PYGZhy{}os\PYGZhy{}compute \PYG{l+s+se}{\PYGZbs{}}
\PYGZhy{}\PYGZhy{}nic port\PYGZhy{}id\PYG{o}{=}\PYG{k}{\PYGZdl{}(}neutron port\PYGZhy{}list \PYG{p}{\textbar{}} grep \PYGZhy{}w eth0\PYGZhy{}vRouter \PYG{p}{\textbar{}} awk \PYG{l+s+s1}{\PYGZsq{}\PYGZob{}print \PYGZdl{}2\PYGZcb{}\PYGZsq{}}\PYG{k}{)} \PYG{l+s+se}{\PYGZbs{}}
\PYGZhy{}\PYGZhy{}nic port\PYGZhy{}id\PYG{o}{=}\PYG{k}{\PYGZdl{}(}neutron port\PYGZhy{}list \PYG{p}{\textbar{}} grep \PYGZhy{}w eth1\PYGZhy{}vRouter \PYG{p}{\textbar{}} awk \PYG{l+s+s1}{\PYGZsq{}\PYGZob{}print \PYGZdl{}2\PYGZcb{}\PYGZsq{}}\PYG{k}{)} \PYG{l+s+se}{\PYGZbs{}}
\PYGZhy{}\PYGZhy{}key\PYGZhy{}name vRouterKey vRouter
Please note that is used to enable the to automatically spawn a , and
- Act as an IPv6 vRouter which advertises the RA (Router Advertisements) with prefix on its internal interface ().
- Forward IPv6 traffic from internal interface ()
SETUP-SVM-20: Verify that image boots up successfully and vRouter has keys properly injected
nova list
nova console\PYGZhy{}log vRouter
Please note that it may take a few minutes for the necessary packages to get installed and keys to be injected.
\PYG{c}{\PYGZsh{} Sample Output}
\PYG{o}{[} 762.884523\PYG{o}{]} cloud\PYGZhy{}init\PYG{o}{[}871\PYG{o}{]}: ec2: \PYG{c}{\PYGZsh{}\PYGZsh{}\PYGZsh{}\PYGZsh{}\PYGZsh{}\PYGZsh{}\PYGZsh{}\PYGZsh{}\PYGZsh{}\PYGZsh{}\PYGZsh{}\PYGZsh{}\PYGZsh{}\PYGZsh{}\PYGZsh{}\PYGZsh{}\PYGZsh{}\PYGZsh{}\PYGZsh{}\PYGZsh{}\PYGZsh{}\PYGZsh{}\PYGZsh{}\PYGZsh{}\PYGZsh{}\PYGZsh{}\PYGZsh{}\PYGZsh{}\PYGZsh{}\PYGZsh{}\PYGZsh{}\PYGZsh{}\PYGZsh{}\PYGZsh{}\PYGZsh{}\PYGZsh{}\PYGZsh{}\PYGZsh{}\PYGZsh{}\PYGZsh{}\PYGZsh{}\PYGZsh{}\PYGZsh{}\PYGZsh{}\PYGZsh{}\PYGZsh{}\PYGZsh{}\PYGZsh{}\PYGZsh{}\PYGZsh{}\PYGZsh{}\PYGZsh{}\PYGZsh{}\PYGZsh{}\PYGZsh{}\PYGZsh{}\PYGZsh{}\PYGZsh{}\PYGZsh{}\PYGZsh{}\PYGZsh{}}
\PYG{o}{[} 762.909634\PYG{o}{]} cloud\PYGZhy{}init\PYG{o}{[}871\PYG{o}{]}: ec2: \PYGZhy{}\PYGZhy{}\PYGZhy{}\PYGZhy{}\PYGZhy{}BEGIN SSH HOST KEY FINGERPRINTS\PYGZhy{}\PYGZhy{}\PYGZhy{}\PYGZhy{}\PYGZhy{}
\PYG{o}{[} 762.931626\PYG{o}{]} cloud\PYGZhy{}init\PYG{o}{[}871\PYG{o}{]}: ec2: \PYG{l+m}{2048} e3:dc:3d:4a:bc:b6:b0:77:75:a1:70:a3:d0:2a:47:a9 \PYG{o}{(}RSA\PYG{o}{)}
\PYG{o}{[} 762.957380\PYG{o}{]} cloud\PYGZhy{}init\PYG{o}{[}871\PYG{o}{]}: ec2: \PYGZhy{}\PYGZhy{}\PYGZhy{}\PYGZhy{}\PYGZhy{}END SSH HOST KEY FINGERPRINTS\PYGZhy{}\PYGZhy{}\PYGZhy{}\PYGZhy{}\PYGZhy{}
\PYG{o}{[} 762.979554\PYG{o}{]} cloud\PYGZhy{}init\PYG{o}{[}871\PYG{o}{]}: ec2: \PYG{c}{\PYGZsh{}\PYGZsh{}\PYGZsh{}\PYGZsh{}\PYGZsh{}\PYGZsh{}\PYGZsh{}\PYGZsh{}\PYGZsh{}\PYGZsh{}\PYGZsh{}\PYGZsh{}\PYGZsh{}\PYGZsh{}\PYGZsh{}\PYGZsh{}\PYGZsh{}\PYGZsh{}\PYGZsh{}\PYGZsh{}\PYGZsh{}\PYGZsh{}\PYGZsh{}\PYGZsh{}\PYGZsh{}\PYGZsh{}\PYGZsh{}\PYGZsh{}\PYGZsh{}\PYGZsh{}\PYGZsh{}\PYGZsh{}\PYGZsh{}\PYGZsh{}\PYGZsh{}\PYGZsh{}\PYGZsh{}\PYGZsh{}\PYGZsh{}\PYGZsh{}\PYGZsh{}\PYGZsh{}\PYGZsh{}\PYGZsh{}\PYGZsh{}\PYGZsh{}\PYGZsh{}\PYGZsh{}\PYGZsh{}\PYGZsh{}\PYGZsh{}\PYGZsh{}\PYGZsh{}\PYGZsh{}\PYGZsh{}\PYGZsh{}\PYGZsh{}\PYGZsh{}\PYGZsh{}\PYGZsh{}\PYGZsh{}}
## Boot Two Other VMs in ipv4-int-network1
[index:boot-two-other-vms-in-ipv4-int-network1] In order to verify that the setup is working, let us create two cirros VMs with interface on the , i.e., connecting to interface for internal network.
We will have to configure appropriate on the VMs’ interface by taking into account the tunneling overhead and any physical switch requirements. If so, push the to the VM either using options or via .
SETUP-SVM-21: Create VM1 on OpenStack Controller Node with hostname
nova boot \PYGZhy{}\PYGZhy{}image cirros\PYGZhy{}0.3.4\PYGZhy{}x86\PYGZus{}64\PYGZhy{}uec \PYGZhy{}\PYGZhy{}flavor m1.tiny \PYG{l+s+se}{\PYGZbs{}}
\PYGZhy{}\PYGZhy{}user\PYGZhy{}data /opt/stack/opnfv\PYGZus{}os\PYGZus{}ipv6\PYGZus{}poc/set\PYGZus{}mtu.sh \PYG{l+s+se}{\PYGZbs{}}
\PYGZhy{}\PYGZhy{}availability\PYGZhy{}zone nova:opnfv\PYGZhy{}os\PYGZhy{}controller \PYG{l+s+se}{\PYGZbs{}}
\PYGZhy{}\PYGZhy{}nic port\PYGZhy{}id\PYG{o}{=}\PYG{k}{\PYGZdl{}(}neutron port\PYGZhy{}list \PYG{p}{\textbar{}} grep \PYGZhy{}w eth0\PYGZhy{}VM1 \PYG{p}{\textbar{}} awk \PYG{l+s+s1}{\PYGZsq{}\PYGZob{}print \PYGZdl{}2\PYGZcb{}\PYGZsq{}}\PYG{k}{)} \PYG{l+s+se}{\PYGZbs{}}
\PYGZhy{}\PYGZhy{}key\PYGZhy{}name vRouterKey VM1
SETUP-SVM-22: Create VM2 on OpenStack Compute Node with hostname
nova boot \PYGZhy{}\PYGZhy{}image cirros\PYGZhy{}0.3.4\PYGZhy{}x86\PYGZus{}64\PYGZhy{}uec \PYGZhy{}\PYGZhy{}flavor m1.tiny \PYG{l+s+se}{\PYGZbs{}}
\PYGZhy{}\PYGZhy{}user\PYGZhy{}data /opt/stack/opnfv\PYGZus{}os\PYGZus{}ipv6\PYGZus{}poc/set\PYGZus{}mtu.sh \PYG{l+s+se}{\PYGZbs{}}
\PYGZhy{}\PYGZhy{}availability\PYGZhy{}zone nova:opnfv\PYGZhy{}os\PYGZhy{}compute \PYG{l+s+se}{\PYGZbs{}}
\PYGZhy{}\PYGZhy{}nic port\PYGZhy{}id\PYG{o}{=}\PYG{k}{\PYGZdl{}(}neutron port\PYGZhy{}list \PYG{p}{\textbar{}} grep \PYGZhy{}w eth0\PYGZhy{}VM2 \PYG{p}{\textbar{}} awk \PYG{l+s+s1}{\PYGZsq{}\PYGZob{}print \PYGZdl{}2\PYGZcb{}\PYGZsq{}}\PYG{k}{)} \PYG{l+s+se}{\PYGZbs{}}
\PYGZhy{}\PYGZhy{}key\PYGZhy{}name vRouterKey VM2
SETUP-SVM-23: Confirm that both the VMs are successfully booted.
nova list
nova console\PYGZhy{}log VM1
nova console\PYGZhy{}log VM2
## Spawn RADVD in ipv6-router
[index:spawn-radvd-in-ipv6-router] Let us manually spawn a daemon inside namespace to simulate an external router. First of all, we will have to identify the namespace and move to the namespace.
Please NOTE that in case of HA (High Availability) deployment model where multiple controller nodes are used, created in step SETUP-SVM-11 could be in any of the controller node. Thus you need to identify in which controller node is created in order to manually spawn daemon inside the namespace in steps SETUP-SVM-24 through SETUP-SVM-30. The following command in Neutron will display the controller on which the is spawned.
neutron l3\PYGZhy{}agent\PYGZhy{}list\PYGZhy{}hosting\PYGZhy{}router ipv6\PYGZhy{}router
Then you login to that controller and execute steps SETUP-SVM-24 through SETUP-SVM-30
SETUP-SVM-24: identify the namespace and move to the namespace
sudo ip netns \PYG{n+nb}{exec }qrouter\PYGZhy{}\PYG{k}{\PYGZdl{}(}neutron router\PYGZhy{}list \PYG{p}{\textbar{}} grep \PYGZhy{}w ipv6\PYGZhy{}router \PYG{p}{\textbar{}} \PYG{l+s+se}{\PYGZbs{}}
awk \PYG{l+s+s1}{\PYGZsq{}\PYGZob{}print \PYGZdl{}2\PYGZcb{}\PYGZsq{}}\PYG{k}{)} bash
SETUP-SVM-25: Upon successful execution of the above command, you will be in the router namespace. Now let us configure the IPv6 address on the <qr-xxx> interface.
\PYG{n+nb}{export }\PYG{n+nv}{router\PYGZus{}interface}\PYG{o}{=}\PYG{k}{\PYGZdl{}(}ip a s \PYG{p}{\textbar{}} grep \PYGZhy{}w \PYG{l+s+s2}{\PYGZdq{}global qr\PYGZhy{}*\PYGZdq{}} \PYG{p}{\textbar{}} awk \PYG{l+s+s1}{\PYGZsq{}\PYGZob{}print \PYGZdl{}7\PYGZcb{}\PYGZsq{}}\PYG{k}{)}
ip \PYGZhy{}6 addr add 2001:db8:0:1::1 dev \PYG{n+nv}{\PYGZdl{}router\PYGZus{}interface}
SETUP-SVM-26: Update the sample file with .
cp /opt/stack/opnfv\PYGZus{}os\PYGZus{}ipv6\PYGZus{}poc/scenario2/radvd.conf /tmp/radvd.\PYG{n+nv}{\PYGZdl{}router\PYGZus{}interface}.conf
sed \PYGZhy{}i \PYG{l+s+s1}{\PYGZsq{}s/\PYGZdl{}router\PYGZus{}interface/\PYGZsq{}}\PYG{n+nv}{\PYGZdl{}router\PYGZus{}interface}\PYG{l+s+s1}{\PYGZsq{}/g\PYGZsq{}} /tmp/radvd.\PYG{n+nv}{\PYGZdl{}router\PYGZus{}interface}.conf
SETUP-SVM-27: Spawn a daemon to simulate an external router. This daemon advertises an IPv6 subnet prefix of using RA (Router Advertisement) on its $router_interface so that interface of automatically configures an IPv6 SLAAC address.
\PYG{n+nv}{\PYGZdl{}radvd} \PYGZhy{}C /tmp/radvd.\PYG{n+nv}{\PYGZdl{}router\PYGZus{}interface}.conf \PYGZhy{}p /tmp/br\PYGZhy{}ex.pid.radvd \PYGZhy{}m syslog
SETUP-SVM-28: Add an IPv6 downstream route pointing to the interface of vRouter.
ip \PYGZhy{}6 route add 2001:db8:0:2::/64 via 2001:db8:0:1:f816:3eff:fe11:1111
SETUP-SVM-29: The routing table should now look similar to something shown below.
ip \PYGZhy{}6 route show
2001:db8:0:1::1 dev qr\PYGZhy{}42968b9e\PYGZhy{}62 proto kernel metric 256
2001:db8:0:1::/64 dev qr\PYGZhy{}42968b9e\PYGZhy{}62 proto kernel metric \PYG{l+m}{256} expires 86384sec
2001:db8:0:2::/64 via 2001:db8:0:1:f816:3eff:fe11:1111 dev qr\PYGZhy{}42968b9e\PYGZhy{}62 proto ra metric \PYG{l+m}{1024} expires 29sec
fe80::/64 dev qg\PYGZhy{}3736e0c7\PYGZhy{}7c proto kernel metric 256
fe80::/64 dev qr\PYGZhy{}42968b9e\PYGZhy{}62 proto kernel metric 256
SETUP-SVM-30: If all goes well, the IPv6 addresses assigned to the VMs would be as shown as follows:
\PYG{c}{\PYGZsh{} vRouter eth0 interface would have the following IPv6 address:}
\PYG{c}{\PYGZsh{} 2001:db8:0:1:f816:3eff:fe11:1111/64}
\PYG{c}{\PYGZsh{} vRouter eth1 interface would have the following IPv6 address:}
\PYG{c}{\PYGZsh{} 2001:db8:0:2::1/64}
\PYG{c}{\PYGZsh{} VM1 would have the following IPv6 address:}
\PYG{c}{\PYGZsh{} 2001:db8:0:2:f816:3eff:fe33:3333/64}
\PYG{c}{\PYGZsh{} VM2 would have the following IPv6 address:}
\PYG{c}{\PYGZsh{} 2001:db8:0:2:f816:3eff:fe44:4444/64}
## Testing to Verify Setup Complete
[index:testing-to-verify-setup-complete] Now, let us to those VMs, e.g. VM1 and / or VM2 and / or vRouter, to confirm that it has successfully configured the IPv6 address using with prefix from .
We use mechanism to achieve .
SETUP-SVM-31: Now we can to VMs. You can execute the following command.
\PYG{c}{\PYGZsh{} 1. Create a floatingip and associate it with VM1, VM2 and vRouter (to the port id that is passed).}
\PYG{c}{\PYGZsh{} Note that the name \PYGZdq{}ext\PYGZhy{}net\PYGZdq{} may work for some installers such as Compass and Joid}
\PYG{c}{\PYGZsh{} Change the name \PYGZdq{}ext\PYGZhy{}net\PYGZdq{} to match the name of external network that an installer creates}
neutron floatingip\PYGZhy{}create \PYGZhy{}\PYGZhy{}port\PYGZhy{}id \PYG{k}{\PYGZdl{}(}neutron port\PYGZhy{}list \PYG{p}{\textbar{}} grep \PYGZhy{}w eth0\PYGZhy{}VM1 \PYG{p}{\textbar{}} \PYG{l+s+se}{\PYGZbs{}}
awk \PYG{l+s+s1}{\PYGZsq{}\PYGZob{}print \PYGZdl{}2\PYGZcb{}\PYGZsq{}}\PYG{k}{)} ext\PYGZhy{}net
neutron floatingip\PYGZhy{}create \PYGZhy{}\PYGZhy{}port\PYGZhy{}id \PYG{k}{\PYGZdl{}(}neutron port\PYGZhy{}list \PYG{p}{\textbar{}} grep \PYGZhy{}w eth0\PYGZhy{}VM2 \PYG{p}{\textbar{}} \PYG{l+s+se}{\PYGZbs{}}
awk \PYG{l+s+s1}{\PYGZsq{}\PYGZob{}print \PYGZdl{}2\PYGZcb{}\PYGZsq{}}\PYG{k}{)} ext\PYGZhy{}net
neutron floatingip\PYGZhy{}create \PYGZhy{}\PYGZhy{}port\PYGZhy{}id \PYG{k}{\PYGZdl{}(}neutron port\PYGZhy{}list \PYG{p}{\textbar{}} grep \PYGZhy{}w eth1\PYGZhy{}vRouter \PYG{p}{\textbar{}} \PYG{l+s+se}{\PYGZbs{}}
awk \PYG{l+s+s1}{\PYGZsq{}\PYGZob{}print \PYGZdl{}2\PYGZcb{}\PYGZsq{}}\PYG{k}{)} ext\PYGZhy{}net

\PYG{c}{\PYGZsh{} 2. To know / display the floatingip associated with VM1, VM2 and vRouter.}
neutron floatingip\PYGZhy{}list \PYGZhy{}F floating\PYGZus{}ip\PYGZus{}address \PYGZhy{}F port\PYGZus{}id \PYG{p}{\textbar{}} grep \PYG{k}{\PYGZdl{}(}neutron port\PYGZhy{}list \PYG{p}{\textbar{}} \PYG{l+s+se}{\PYGZbs{}}
grep \PYGZhy{}w eth0\PYGZhy{}VM1 \PYG{p}{\textbar{}} awk \PYG{l+s+s1}{\PYGZsq{}\PYGZob{}print \PYGZdl{}2\PYGZcb{}\PYGZsq{}}\PYG{k}{)} \PYG{p}{\textbar{}} awk \PYG{l+s+s1}{\PYGZsq{}\PYGZob{}print \PYGZdl{}2\PYGZcb{}\PYGZsq{}}
neutron floatingip\PYGZhy{}list \PYGZhy{}F floating\PYGZus{}ip\PYGZus{}address \PYGZhy{}F port\PYGZus{}id \PYG{p}{\textbar{}} grep \PYG{k}{\PYGZdl{}(}neutron port\PYGZhy{}list \PYG{p}{\textbar{}} \PYG{l+s+se}{\PYGZbs{}}
grep \PYGZhy{}w eth0\PYGZhy{}VM2 \PYG{p}{\textbar{}} awk \PYG{l+s+s1}{\PYGZsq{}\PYGZob{}print \PYGZdl{}2\PYGZcb{}\PYGZsq{}}\PYG{k}{)} \PYG{p}{\textbar{}} awk \PYG{l+s+s1}{\PYGZsq{}\PYGZob{}print \PYGZdl{}2\PYGZcb{}\PYGZsq{}}
neutron floatingip\PYGZhy{}list \PYGZhy{}F floating\PYGZus{}ip\PYGZus{}address \PYGZhy{}F port\PYGZus{}id \PYG{p}{\textbar{}} grep \PYG{k}{\PYGZdl{}(}neutron port\PYGZhy{}list \PYG{p}{\textbar{}} \PYG{l+s+se}{\PYGZbs{}}
grep \PYGZhy{}w eth1\PYGZhy{}vRouter \PYG{p}{\textbar{}} awk \PYG{l+s+s1}{\PYGZsq{}\PYGZob{}print \PYGZdl{}2\PYGZcb{}\PYGZsq{}}\PYG{k}{)} \PYG{p}{\textbar{}} awk \PYG{l+s+s1}{\PYGZsq{}\PYGZob{}print \PYGZdl{}2\PYGZcb{}\PYGZsq{}}

\PYG{c}{\PYGZsh{} 3. To ssh to the vRouter, VM1 and VM2, user can execute the following command.}
ssh \PYGZhy{}i \PYGZti{}/vRouterKey fedora@\PYGZlt{}floating\PYGZhy{}ip\PYGZhy{}of\PYGZhy{}vRouter\PYGZgt{}
ssh \PYGZhy{}i \PYGZti{}/vRouterKey cirros@\PYGZlt{}floating\PYGZhy{}ip\PYGZhy{}of\PYGZhy{}VM1\PYGZgt{}
ssh \PYGZhy{}i \PYGZti{}/vRouterKey cirros@\PYGZlt{}floating\PYGZhy{}ip\PYGZhy{}of\PYGZhy{}VM2\PYGZgt{}
If everything goes well, will be successful and you will be logged into those VMs. Run some commands to verify that IPv6 addresses are configured on interface.
SETUP-SVM-32: Show an IPv6 address with a prefix of
ip address show
SETUP-SVM-33: ping some external IPv6 address, e.g.
ping6 2001:db8:0:1::1
If the above ping6 command succeeds, it implies that was able to successfully forward the IPv6 traffic to reach external .
# IPv6 Post Installation Procedures
[index:ipv6-post-installation-procedures] Congratulations, you have completed the setup of using a service VM to act as an IPv6 vRouter. You have validated the setup based on the instruction in previous sections. If you want to further test your setup, you can among , , and .
This setup allows further open innovation by any 3rd-party. For more instructions and documentations, please refer to:
1. IPv6 Configuration Guide (HTML): http://artifacts.opnfv.org/ipv6/docs/setupservicevm/index.html
2. IPv6 User Guide (HTML): http://artifacts.opnfv.org/ipv6/docs/gapanalysis/index.html
# Automated post installation activities
[index:automated-post-installation-activities] Refer to the relevant testing guides, results, and release notes of Yardstick Project.