# OPNFV Configuration Guide
OPNFV
February 01, 2016
[index::doc]
# Abstract
[abstract:abstract][abstract::doc][abstract:opnfv-configuration-guide] This document provides guidance and instructions for the configuration of the Brahmaputra release of OPNFV.
The release includes four installer tools leveraging different technologies; Apex, Compass4nfv, Fuel and JOID, which deploy components of the platform.
This document provides a guide for the selection of tools and components including guidelines for how to deploy and configure the platform to an operational state.
# Configuration Options
[configoptions:configuration-options][configoptions::doc] OPNFV provides a variety of virtual infrastructure deployments called scenarios designed to host virtualised network functions (VNF’s). Each scenario provide specific capabilities and/or components aimed to solve specific problems for the deployment of VNF’s. A scenario may include components such as OpenStack, OpenDaylight, OVS, KVM etc. where each scenario will include different source components or configurations.
## OPNFV Scenario’s
[configoptions:opnfv-scenario-s] Each OPNFV scenario provides unique features and capabilities, it is important to understand your target platform capabilities before installing and configuring your target scenario. This configuration guide outlines how to install and configure components in order to enable the features you require.
Scenarios are implemented as deployable compositions through integration with an installation tool. OPNFV supports multiple installation tools and for any given release not all tools will support all scenarios. While our target is to establish parity across the installation tools to ensure they can provide all scenarios, the practical challenge of achieving that goal for any given feature and release results in some disparity.
### Scenario Naming
[configoptions:scenario-naming] In OPNFV scenarios are identified by short scenario names, these names follow a scheme that identifies the key components and behaviours of the scenario. The rules for scenario naming are as follows:
os-[controller]-[feature]-[mode]-[option]
Details of the fields are
- os: mandatory
  - Refers to the platform type used
  - possible value: os (OpenStack)
- [
  controller]: mandatory
  - Refers to the SDN controller integrated in the platform
  - example values: nosdn, ocl, odl, onos
  - [
    feature]: mandatory
    - Refers to the feature projects supported by the scenario
    - example values: nofeature, kvm, ovs
  - [
    mode]: mandatory
    - Refers to the deployment type, which may include for instance high availability
    - possible values: ha, noha
  - [
    option]: optional
    - Used for the scenarios those do not fit into naming scheme.
    - The optional field in the short scenario name should not be included if there is no optional scenario.
Some examples of supported scenario names are:
- os-nosdn-kvm-noha
  - This is an OpenStack based deployment using neutron including the OPNFV enhanced KVM hypervisor
- os-odl_l2-nofeature-ha
  - This is an OpenStack deployment in high availability mode including OpenDaylight layer2 networking
- os-onos-kvm_ovs-noha
  - This is an OpenStack deployment using ONOS including OPNFV enhanced KVM and OVS versions
### Installing your scenario
[configoptions:installing-your-scenario] There are two main methods of deploying your target scenario, one method is to follow this guide which will walk you through the process of deploying to your hardware using scripts or ISO images, the other method is to set up a Jenkins slave and connect your infrastructure to the OPNFV Jenkins master.
For the purposes of evaluation and development a number of Brahmaputra scenarios are able to be deployed virtually to mitigate the requirements on physical infrastructure. Details and instructions on performing virtual deployments can be found in the installer specific installation instructions.
To set up a Jenkins slave for automated deployment to your lab, refer to the Jenkins slave connect guide.
### Brahmaputra scenario overeview
[configoptions:brahmaputra-scenario-overeview] The following table provides an overview of the installation tools and available scenario’s in the Brahmaputra release of OPNFV.

This document will describe how to install and configure your target OPNFV scenarios. Remember to check the associated validation procedures section following your installation for details of the use cases and tests that have been run.
# Installer Configuration
[installer-config:installer-configuration][installer-config::doc] The following sections describe the per installer configuration options. Further details for each installer are captured in the referred project documentation.
## <Project> configuration
[installer-config:project-configuration] Add a brief introduction to configure OPNFV with this specific installer
### Pre-configuration activities
[installer-config:pre-configuration-activities] Describe specific pre-configuration activities. Refer to Installations guide and release notes
### Hardware configuration
[installer-config:hardware-configuration] Describe the hardware configuration needed for this specific installer
### Jumphost configuration
[installer-config:jumphost-configuration] Describe intial Jumphost configuration (network and software)needed in order to deploy the installer
### Platform components configuration
[installer-config:platform-components-configuration] Describe the configuration of each component in the installer
# Deploy JOID in your LAB
[installer-config:deploy-joid-in-your-lab] minimum 2 networks
0em
NOTE: JOID support multiple isolated networks for data as well as storage. Based on your network options for Openstack.
0em
0em
0em
NOTE: Above configuration is minimum and for better performance and usage of the Openstack please consider higher spec for each nodes.
Make sure all servers are connected to top of rack switch and configured accordingly. No DHCP server should be up and configured. Only gateway at eth0 and eth1 network should be configure to access the network outside your lab.
1. Install Ubuntu 14.04 LTS server version of OS on the nodes. 2. Install the git and bridge-utils packages on the server and configure minimum two bridges on jump host:
brAdm and brPublic cat /etc/network/interfaces
0em
NOTE: If you choose to use the separate network for management, data and storage then you need to create bridge for each interface. In case of VLAN tags use the appropriate network on jump-host depend upon VLAN ID on the interface.
Get the joid code from gerritt
git clone https://gerrit.opnfv.org/gerrit/p/joid.git
cd joid/ci
Enable MAAS
Create a directory in maas/<company name>/<pod number>/ for example
mkdir maas/intel/pod7/
Copy files from pod5 to pod7
cp maas/intel/pod5/* maas/intel/pod7/
4 files will get copied: deployment.yaml environments.yaml interfaces.host lxc-add-more-interfaces
This file has been used to configure your maas and bootstrap node in a VM. Comments in the file are self explanatory and we expect fill up the information according to match lab infrastructure information. Sample deployment.yaml can be found at https://gerrit.opnfv.org/gerrit/gitweb?p=joid.git;a=blob;f=ci/maas/intel/pod5/deployment.yaml
under section case $3 add the intelpod7 section and make sure you have information provided correctly. Before example consider your network has 192.168.1.0/24 your default network. and eth1 is on public network which will be used to assign the floating ip.
0em
NOTE: If you are using seprate data network then add this line below also along with other changes. which represents network 10.4.9.0/24 will be used for data network for openstack
under section case $1 add the intelpod7 section and make sure you have information provided correctly.
0em
NOTE: If you are using VLAN tags or more network for data and storage then make sure you modify the case $1 section under Enable vlan interface with maas appropriately. In the example below eth2 has been used as separate data network for tenants in openstack with network 10.4.9.0/24 on compute and control nodes.
0em
Once you have done the change in above section then run the following commands to do the automatic deployments.
After integrating the changes as mentioned above run the MAAS install. Suppose you name the integration lab as intelpod7 then run the below commands to start the MAAS deployment.
0em
NOTE: Possible options are as follows:
0em
By default debug is enabled in script and error messages will be printed on ssh terminal where you are running the scripts.
To access of any control or compute nodes. juju ssh for example to login into openstack-dashboard container.
0em
By default juju will add the Ubuntu user keys for authentication into the deployed server and only ssh access will be available.
# Feature Configuration
[feature-config:feature-configuration][feature-config::doc] The following sections describe the configuration options for specific platform features provided in Brahmaputra. Further details for each feature are captured in the referred project documentation.
## Configuring SDNVPN features
[feature-config:configuring-sdnvpn-features] Stuff about configuring SDNVPN features...
# Post Configuration Activities
[post-install:post-configuration-activities][post-install::doc] This section describes the post configuration activitites that will allow you to validate the success of your configuration. Further details may be found in the referred project specific documentation.
## Functional testing Installation
[post-install:functional-testing-installation] Pull the Functest Docker image from the Docker hub:
\PYGZdl{} docker pull opnfv/functest:brahmaputra.1.0
Check that the image is available:
\PYGZdl{} docker images
Run the docker container giving the environment variables:
\PYGZhy{} INSTALLER\PYGZus{}TYPE. Possible values are \PYGZdq{}apex\PYGZdq{}, \PYGZdq{}compass\PYGZdq{}, \PYGZdq{}fuel\PYGZdq{} or \PYGZdq{}joid\PYGZdq{}.
\PYGZhy{} INSTALLER\PYGZus{}IP. each installer has its installation strategy.
Functest may need to know the IP of the installer to retrieve the credentials (e.g. usually “10.20.0.2” for fuel, not neede for joid...).
The minimum command to create the Functest docker file can be described as follows:
docker run \PYGZhy{}it \PYGZhy{}e \PYGZdq{}INSTALLER\PYGZus{}IP=10.20.0.2\PYGZdq{} \PYGZhy{}e \PYGZdq{}INSTALLER\PYGZus{}TYPE=fuel\PYGZdq{} opnfv/functest:brahmaputra.1.0 /bin/bash
Optionally, it is possible to precise the container name through the option –name:
docker run \PYGZhy{}\PYGZhy{}name \PYGZdq{}CONTAINER\PYGZus{}NAME\PYGZdq{} \PYGZhy{}it \PYGZhy{}e \PYGZdq{}INSTALLER\PYGZus{}IP=10.20.0.2\PYGZdq{} \PYGZhy{}e \PYGZdq{}INSTALLER\PYGZus{}TYPE=fuel\PYGZdq{} opnfv/functest:brahmaputra.1.0 /bin/bash
It is also possible to to indicate the path of the OpenStack creds using -v:
docker run \PYGZhy{}it \PYGZhy{}e \PYGZdq{}INSTALLER\PYGZus{}IP=10.20.0.2\PYGZdq{} \PYGZhy{}e \PYGZdq{}INSTALLER\PYGZus{}TYPE=fuel\PYGZdq{} \PYGZhy{}v \PYGZlt{}path\PYGZus{}to\PYGZus{}your\PYGZus{}local\PYGZus{}creds\PYGZus{}file\PYGZgt{}:/home/opnfv/functest/conf/openstack.creds opnfv/functest:brahmaputra.1.0 /bin/bash
The local file will be mounted in the container under /home/opnfv/functest/conf/openstack.creds
After the run command the prompt appears which means that we are inside the container and ready to run Functest.
Inside the container, the following directory structure should be in place:
{}`\PYGZhy{}\PYGZhy{} home
    {}`\PYGZhy{}\PYGZhy{} opnfv
      \textbar{}\PYGZhy{}\PYGZhy{} functest
      \textbar{} \textbar{}\PYGZhy{}\PYGZhy{} conf
      \textbar{} \textbar{}\PYGZhy{}\PYGZhy{} data
      \textbar{} {}`\PYGZhy{}\PYGZhy{} results
      {}`\PYGZhy{}\PYGZhy{} repos
        \textbar{}\PYGZhy{}\PYGZhy{} bgpvpn
        \textbar{}\PYGZhy{}\PYGZhy{} functest
        \textbar{}\PYGZhy{}\PYGZhy{} odl\PYGZus{}integration
        \textbar{}\PYGZhy{}\PYGZhy{} rally
        \textbar{}\PYGZhy{}\PYGZhy{} releng
        {}`\PYGZhy{}\PYGZhy{} vims\PYGZhy{}test
Basically the container includes:
- Functest directory to store the configuration (the OpenStack creds are paste in /home/opngb/functest/conf), the data (images neede for test for offline testing), results (some temporary artifacts may be stored here)
- Repositories: the functest repository will be used to prepare the environment, run the tests. Other repositories are used for the installation of the tooling (e.g. rally) and/or the retrieval of feature projects scenarios (e.g. bgpvpn)
The arborescence under the functest repo can be described as follow:
.
  \textbar{}\PYGZhy{}\PYGZhy{} INFO
  \textbar{}\PYGZhy{}\PYGZhy{} LICENSE
  \textbar{}\PYGZhy{}\PYGZhy{} commons
  \textbar{} \textbar{}\PYGZhy{}\PYGZhy{} ims
  \textbar{} \textbar{}\PYGZhy{}\PYGZhy{} mobile
  \textbar{} {}`\PYGZhy{}\PYGZhy{} traffic\PYGZhy{}profile\PYGZhy{}guidelines.rst
  \textbar{}\PYGZhy{}\PYGZhy{} docker
  \textbar{} \textbar{}\PYGZhy{}\PYGZhy{} Dockerfile
  \textbar{} \textbar{}\PYGZhy{}\PYGZhy{} common.sh
  \textbar{} \textbar{}\PYGZhy{}\PYGZhy{} prepare\PYGZus{}env.sh
  \textbar{} \textbar{}\PYGZhy{}\PYGZhy{} requirements.pip
  \textbar{} {}`\PYGZhy{}\PYGZhy{} run\PYGZus{}tests.sh
  \textbar{}\PYGZhy{}\PYGZhy{} docs
  \textbar{} \textbar{}\PYGZhy{}\PYGZhy{} configguide
  \textbar{} \textbar{}\PYGZhy{}\PYGZhy{} functest.rst
  \textbar{} \textbar{}\PYGZhy{}\PYGZhy{} images
  \textbar{} {}`\PYGZhy{}\PYGZhy{} userguide
  {}`\PYGZhy{}\PYGZhy{} testcases
      \textbar{}\PYGZhy{}\PYGZhy{} Controllers
      \textbar{}\PYGZhy{}\PYGZhy{} VIM
      \textbar{}\PYGZhy{}\PYGZhy{} \PYGZus{}\PYGZus{}init\PYGZus{}\PYGZus{}.py
      \textbar{}\PYGZhy{}\PYGZhy{} config\PYGZus{}functest.py
      \textbar{}\PYGZhy{}\PYGZhy{} config\PYGZus{}functest.yaml
      \textbar{}\PYGZhy{}\PYGZhy{} functest\PYGZus{}utils.py
      \textbar{}\PYGZhy{}\PYGZhy{} functest\PYGZus{}utils.pyc
      \textbar{}\PYGZhy{}\PYGZhy{} vIMS
      {}`\PYGZhy{}\PYGZhy{} vPing
We may distinguish 4 different folders:
- commons: it is a folder dedicated to store traffic profile or any test inputs that could be reused by any test project
- docker: this folder includes the scripts that will be used to setup the environment and run the tests
- docs: this folder includes the user and installation/configuration guide
- testcases: this folder includes the scripts required by Functest internal test cases
Firstly run the script to install functest environment:
\PYGZdl{} \PYGZdl{}\PYGZob{}repos\PYGZus{}dir\PYGZcb{}/functest/docker/prepare\PYGZus{}env.sh
NOTE: ${repos_dir} is a default environment variable inside the docker container, which points to /home/opnfv/repos
Run the script to start the tests:
\PYGZdl{} \PYGZdl{}\PYGZob{}repos\PYGZus{}dir\PYGZcb{}/functest/docker/run\PYGZus{}tests.sh
## <Project> post installation procedures
[post-install:project-post-installation-procedures] Add a brief introduction to the methods of validating the installation according to this specific installer or feature.
### Automated post installation activities
[post-install:automated-post-installation-activities] Describe specific post installation activities performed by the OPNFV deployment pipeline including testing activities and reports. Refer to the relevant testing guides, results, and release notes.
note: this section should be singular and derived from the test projects once we have one test suite to run for all deploy tools. This is not the case yet so each deploy tool will need to provide (hopefully very simillar) documentation of this.
### <Project> post configuration procedures
[post-install:project-post-configuration-procedures] Describe any deploy tool or feature specific scripts, tests or procedures that should be carried out on the deployment post install and configuration in this section.
### Platform components validation
[post-install:platform-components-validation] Describe any component specific validation procedures necessary for your deployment tool in this section.