# OPNFV deployment tools common requirements
OPNFV
February 25, 2016
[index::doc]
# UX requirements
[userexperience:opnfv-deployment-tools-common-requirements][userexperience::doc][userexperience:ux-requirements] Release: OPNFV Brahmaputra
Requirements for a common user-experience created by the deployment tools.
## High availability requirements
[userexperience:high-availability-requirements]
- GENESIS-9: Installers shall support the deployment of OpenStack with High-Availability (for those components that support it in Liberty) on 3 or more control nodes. Functest tests should be able to verify that the HA is enabled and functional.
- GENESIS-71: Hitless hardware upgrade: Increase size of a deployment in terms of compute nodes (add additional compute nodes) without service interruption. This requirement doesn’t mandate upgrade/increasing the size of the control node cluster.
## Network setup and configuration related requirements
[userexperience:network-setup-and-configuration-related-requirements]
- GENESIS-20: Automatically populate discovered servers into install tool (reduce user-intervention to a minimum).
- GENESIS-28: Installers should support a common configuration file (e.g. kickstart file) per platform/role, so that the installed OS can be customized for hardware and role.
- GENESIS-43: Neutron DHCP servers should be configured in HA per tenant.
- GENESIS-44: SDN Controller layer 3 forwarding support.
- GENESIS-61: Support layer 1/2 networking configuration.
- GENESIS-62: Support logical networks for target system.
- GENESIS-72: Support L3-neutron agent as an option for L3.
- GENESIS-69: Provide isolated compute node resources for CEPH OSD.
## Versioning requirements
[userexperience:versioning-requirements]
GENESIS-12: Installers should track/control all versions of all components pulled from external sources (user should be able to identify the versions and origins of all software components deployed).
## System definition and system configuration requirements
[userexperience:system-definition-and-system-configuration-requirements]
- GENESIS-16: Common ability to input site, topology, and server information.
- GENESIS-17: User-configurable parameters available via config files.
- GENESIS-18: Allow assignment of different roles to servers, so that hardware and software can be configured according to the role.
- GENESIS-19: Deployment tool to provide for automatic device discovery.
- GENESIS-25: Installers should configure NTP servers on the servers for clock synchronization.
- GENESIS-40: Hardware replacement.
## Requirements pertaining to the qualities of the deployment process
[userexperience:requirements-pertaining-to-the-qualities-of-the-deployment-process]
- GENESIS-74: Installers which create a build for Brahmaputra, should create the build as an “all-in-one” build. The the build process of the installer creates a single entity (e.g. ISO) - which has all the artifacts considered and required by all the projects for Brahmaputra packaged in. Or in other terms and as an example: If there are 4 different versions of OVS - all these 4 versions would be contained in the “all in one build”. Note: This requirement only applies to installers which support a “build” phase (i.e. create a bootable image, like an iso-image from the different artifacts required).
- GENESIS-31: Installers to be agnostic to type of hard drives used.
## Security related requirements
[userexperience:security-related-requirements]
- GENESIS-23: Installers should enable Mandatory Access Control by default. Installers should enable MAC either using SElinux or AppArmour.
- GENESIS-24: Installers should install ssh keys on servers so that key-based login can be used for administration.
## Testing related requirements
[userexperience:testing-related-requirements]
## Installation method related requirements
[userexperience:installation-method-related-requirements]
- GENESIS-39: Ability to install with upstream artifacts.
- GENESIS-38: Installers should supply a script or set of scripts (“deploy.sh”) to automatically install the jumphost (from there, the entire OPNFV system is automatically installed).
- GENESIS-42: Installers should support offline deployment. Jump host may have Internet access, but the installers should support offline installation on target hosts during the deployment phase (either manually or automatically).
## Documentation related requirements
[userexperience:documentation-related-requirements]
- GENESIS-34: Installers should provide a user guide.
- GENESIS-35: Installers should provide release notes for an OPNFV release as part of the documentation provided.
# Target system requirements
[system:target-system-requirements][system::doc] Release: OPNFV Brahmaputra
This document lists requirements for the target system that an installer creates. Different from the requirements document on user-experience, this document focuses on the key hardware and software components the different deployment tools install and/or configure.
## Minimum base Operating System distribution supported:
[system:minimum-base-operating-system-distribution-supported]
GENESIS-4: Installers should support either Centos 7 or Ubuntu 14.04 as target system base OS.
## Components/features installed for OpenStack:
[system:components-features-installed-for-openstack]
GENESIS-53: OpenStack Heat should be installed.
## Minimum base OpenStack distribution supported:
[system:minimum-base-openstack-distribution-supported]
GENESIS-7: Installers should support OpenStack Liberty release.
## SDN Controller:
[system:sdn-controller]
- GENESIS-6: Installers should support OpenDaylight Beryllium Release.
- GENESIS-49: Installers should support ONOSFW.
## VM Controller:
[system:vm-controller]
## Hypervisor:
[system:hypervisor]
GENESIS-8: Installers should support KVM hypervisor.
## Virtual forwarder:
[system:virtual-forwarder]
# Deployment tools support matrix
[component-support:deployment-tools-support-matrix][component-support::doc] This document provides a summary view of the features and capabilities of deployment tools (a.k.a. “installers”) which are expected to be common for all deployment tools.
The tables below only show a short abbreviation of the requirement. For details, please refer to detailed UX-requirements and system-requirements documents.
## Target system requirements
[component-support:target-system-requirements]
|L|L|L|L|L|
& & & &
GENESIS-4 - Centos7 or Ubuntu 14.04 & yes & yes & yes & yes
GENESIS-53 - OpenStack Heat & yes & & yes & yes
GENESIS-6 - OpenDaylight Beryllium & yes & & yes & yes
GENESIS-49 - ONOSFW & yes & & yes & yes
GENESIS-8 - KVM Hypervisor & yes & & yes & yes
## User experience requirements
[component-support:user-experience-requirements]
|L|L|L|L|L|
& & & &
GENESIS-9 - OpenStack HA & yes & & yes & yes
GENESIS-71 - Hitless hardware upgrade & yes & & yes & yes
GENESIS-20 - Server discovery integrated & yes & & yes & yes
GENESIS-28 - Common configuration file & yes & & yes & yes
GENESIS-43 - DHCP server HA per tenant & yes & & yes & yes
GENESIS-44 - SDN Controller L3 & yes & & yes & no
GENESIS-61 - L1/2 networking config & yes & & yes & yes
GENESIS-62 - Logical networks & yes & & yes & yes
GENESIS-72 - L3-neutron agent & yes & & yes & yes
GENESIS-69 - Isolated CEPH OSD & yes & & yes & yes
GENESIS-12 - Version control for components & yes & & yes & yes
GENESIS-16 - Common inventory config & yes & & yes & yes
GENESIS-17 - User-facing config files & yes & & yes & yes
GENESIS-18 - Server roles & yes & & yes & yes
GENESIS-19 - Automatic device discovery & yes & & yes & yes
GENESIS-25 - NTP config & yes & & yes & yes
GENESIS-40 - Hardware replacement support & yes & & yes & yes
GENESIS-74 - “all-in-one” build & yes & & yes & n/a
GENESIS-31 - Agnostic to type of hard drive & yes & & yes & yes
GENESIS-23 - Mandatory Access Control & yes & & yes & yes
GENESIS-24 - Install ssh keys & yes & & yes & yes
GENESIS-39 - Use artifacts from upstream & yes & & yes & yes
GENESIS-38 - Deploy script for jumphost & yes & & yes & yes
GENESIS-42 - Offline deployment & yes & & yes & yes
GENESIS-34 - User guide & yes & & yes & yes
GENESIS-35 - Release notes & yes & & yes & yes
# Key artifacts and their locations
[artifacts-location:key-artifacts-and-their-locations][artifacts-location::doc] Release: OPNFV Brahmaputra
## VM manager components
[artifacts-location:vm-manager-components]
OpenStack:
location: http://docs.openstack.org/releases/releases/liberty.html joid_location: cloud-archive:liberty release: Liberty
## Network controller components
[artifacts-location:network-controller-components]
- OpenDaylight Controller:
  location: `https://nexus.opendaylight.org/content/repositories/staging/org/opendaylight/integration/distribution-karaf/0.4.0-Beryllium-RC2/distribution-karaf-0.4.0-Beryllium-RC2.tar.gz` release: Beryllium RC2
- OpenDaylight SFC:
  location: https://www.dropbox.com/s/6w76eo7loltvvb5/openstack.net-virt-sfc-karaf-1.2.1-SNAPSHOT.zip
- ONOS Controller:
  location: http://downloads.onosproject.org/nightly/onos-1.4.0-rc2.tar.gz release: Emu 1.4.0-rc2
## vSwitch components
[artifacts-location:vswitch-components]
OVS NSH build:
location: https://github.com/openvswitch/ovs.git commit: 121daded51b9798fe3722824b27a05c16806cbd1
OVS build:
joid_location: cloud-archive:liberty release: 1.4.0
## JOID components
[artifacts-location:joid-components]
MAAS:
location: ppa:maas/stable release: 1.9.0
JUJU:
location: ppa:juju/stable release: 1.25.3
CHARM:
location: https://code.launchpad.net/openstack-charmers
charm: “cs:trusty/juju-gui” charm: “cs:trusty/ubuntu” charm: “cs:trusty/mongodb” branch: “lp:openstack-charmers/charms/trusty/percona-cluster/next” branch: “lp:openstack-charmers/charms/trusty/hacluster/next” branch: “lp:openstack-charmers/charms/trusty/ceilometer/next” branch: “lp:openstack-charmers/charms/trusty/ceilometer-agent/next” branch: “lp:openstack-charmers/charms/trusty/heat/next” branch: lp:openstack-charmers/charms/trusty/ceph/next branch: lp:openstack-charmers/charms/trusty/ceph-osd/next branch: lp:openstack-charmers/charms/trusty/ceph-radosgw/next branch: lp:openstack-charmers/charms/trusty/cinder/next branch: lp:openstack-charmers/charms/trusty/cinder-ceph/next branch: lp:openstack-charmers/charms/trusty/rabbitmq-server/next branch: lp:openstack-charmers/charms/trusty/keystone/next branch: lp:openstack-charmers/charms/trusty/openstack-dashboard/next branch: lp:openstack-charmers/charms/trusty/nova-compute/next branch: lp:openstack-charmers/charms/trusty/nova-cloud-controller/next branch: lp:openstack-charmers/charms/trusty/neutron-api/next branch: lp:openstack-charmers/charms/trusty/neutron-gateway/next branch: lp:openstack-charmers/charms/trusty/odl-controller/next branch: lp:openstack-charmers/charms/trusty/glance/next branch: lp:narindergupta/charms/trusty/promise/trunk branch: lp:openstack-charmers/charms/trusty/neutron-api-odl/next branch: lp:openstack-charmers/charms/trusty/openvswitch-odl/trunk branch: lp:charmers/charms/precise/zookeeper/trunk branch: lp:stub/charms/trusty/cassandra/noauthentication branch: lp:sdn-charmers/charms/trusty/contrail-configuration/trunk branch: lp:sdn-charmers/charms/trusty/contrail-control/trunk branch: lp:sdn-charmers/charms/trusty/contrail-analytics/trunk branch: lp:sdn-charmers/charms/trusty/contrail-webui/trunk branch: lp:opnfv-team/charms/trusty/neutron-api-contrail/trunk branch: lp:opnfv-team/charms/trusty/neutron-contrail/trunk branch: lp:sdn-charmers/charms/trusty/keepalived/trunk branch: “lp:wuwenbin2/onosfw/onos-controller” branch: “lp:wuwenbin2/onosfw/neutron-api-onos” branch: “lp:wuwenbin2/onosfw/openvswitch-onos”