# ONOSFW User Guide
OPNFV
August 15, 2016
[index::doc]
# ONOSFW User Guide Manaully
[feature.usage:onosfw-user-guide-manaully][feature.usage:onosfw-user-guide][feature.usage::doc]0
## Abstract
[feature.usage:abstract] This document describes the user guide instruction for onosfw project, including env setup and test case.
## License
[feature.usage:license] ONOSFW User Guide Manaully Docs (c) by Lucius (HUAWEI)
ONOSFW User Guide Manaully Docs are licensed under a Creative Commons Attribution 4.0 International License. You should have received a copy of the license along with this. If not, see <http://creativecommons.org/licenses/by/4.0/>.
## Version history
[feature.usage:version-history]
|L|L|L|L|
Date & Ver. & Author & Comment
2016-01-21 & 1.0.0 & Lucius (HUAWEI) & Rewritten for ONOSFW C release
## Introduction
[feature.usage:introduction] ONOSFW addresses integrating an SDN controller of choice based on a target applications or use cases within the OPNFV defined NFVI and VIM framework. In the Colorado release, in addition to the features in the Brahmaputra release, ONOSFW has included more functions in the Goldeneys of ONOS, and added service Function Chaining scenario by integrating the networking-sfc capability of openstack. Therefore, both features and scenarios configurations are described.
## ONOSFW User Guide Manaully
[feature.usage:id1]
### ONOSFW Environment Setup
[feature.usage:onosfw-environment-setup]
initialize environment:
initialize openstack：delete allthe network, instance and router.
initialize ovs：delete managerand bridge by the following command：
ovs-vsctl del-manager
ovs-vsctl del-br “bridge name”
restart ONOS，install feature:
feature:install onos-openflow-base
feature:install onos-openflow
feature:install onos-ovsdatabase
feature:install onos-ovsdb-base
feature:install onos-drivers-ovsdb
feature:install onos-ovsdb-provider-host
feature:install onos-app-vtn-onosfw
set the external port name:
ONOS command：externalportname-set –n “external port name”
create provider network:
set manager on compute node and network node: ovs-vsctl set-manager tcp:“onos ip”:6640
1. create basic networks and instances on openstack dashboard to verify L2/L3 function
2. create basic scenarios to verify SFC functions.
### Scenario Supported
[feature.usage:scenario-supported]
- L2 scene:
  - Live Migration
  - With between same node under the same tenant and network wether the vm is conneted
  - With between different nodes under the same tenant and network wether the vm is conneted
  - With between same node under the same tenant and different network wether the vm is not conneted
  - With between different nodes under the same tenant and different network wether the vm is not conneted
  - With between same nodes under the different tenant and different network wether the vm is not conneted
  - With between different nodes under the different tenant and different network wether the vm is not conneted
- L3 scene:
  - With between same node under the same tenant and network wether the vm is conneted
  - With between different nodes under the same tenant and network wether the vm is conneted
  - With between same node under the same tenant and different network wether the vm is conneted
  - With between different nodes under the same tenant and different network wether the vm is conneted
  - With between same nodes under the different tenant and different network wether the vm is not conneted
  - With between different nodes under the different tenant and different network wether the vm is not conneted
  VM can ping external network well
- SFC scene:
  - Create 3-4 VNF-nodes service chain, verify with traffic
  - Remove service chain, display service chain info
  - Insert a node(vnf) in the chain, and verify with traffic
  - Remove a node from the chain and verify with traffic
  - Get service chain status
### ONOSFW Demo Video
[feature.usage:onosfw-demo-video]
ONOSFW L2 Function Flash video：https://www.youtube.com/watch?v=7bxjWrR4peI
ONOSFW L2 Function Demo video：https://www.youtube.com/watch?v=qP8nPYhz_Mo
ONOSFW L3 Function Demo video：https://www.youtube.com/watch?v=R0H-IibpVxw
ONOSFW SFC Function Demo video: https://www.youtube.com/watch?v=2vWusqd3WJ4
Revision:
Author
Lucius(lukai1@huawei.com)
Build date: August 15, 2016
Revision:
Author
Lucius(lukai1@huawei.com)
Build date: August 15, 2016