# fuel-os-nosdn-ovs-ha overview and description
OPNFV
August 12, 2016
[index::doc]
# Introduction
[scenario.description:introduction][scenario.description::doc][scenario.description:fuel-os-nosdn-ovs-ha-overview-and-description] This scenario replaces the DPDK-enabled Open vSwitch component with a later version - 2.5.90 based on DPDK 16.07.
# Scenario components and composition
[scenario.description:scenario-components-and-composition] The scenario currently supports the Fuel and Apex installers.
# Scenario usage overview
[scenario.description:scenario-usage-overview] After installation use of the scenario requires no further action by the user. Traffic on the private network will automatically be processed by the upgraded DPDK datapath.
# Limitations, Issues and Workarounds
[scenario.description:limitations-issues-and-workarounds] The same limitations that apply to using Fuel DPDK-enabled interfaces also apply when using this scenario. Including:
- Fuel9 OVS-DPDK support works only for VLAN segmentation.
- Only interfaces running the private network (and no other network) can be supported so each node needs a separate interface dedicated to the private network.
- The nodes with dpdk enabled interfaces will need to have hugepages configured and some cores reserved for dpdk.
# References
[scenario.description:references] For more information on the OPNFV Colorado release, please visit http://www.opnfv.org/colorado