# OVSNFV Guides and Installation
OPNFV
February 25, 2016
[index::doc]
# Open vSwitch
[featureusage:ovsnfv-guides-and-installation][featureusage::doc][featureusage:open-vswitch] Open vSwtich (OVS) is a software switch commonly used in OpenStack deployments to replace Linux bridges as it offers advantages in terms of mobility, hardware integration and use by network controllers.
## Supported OPNFV Installers
[featureusage:supported-opnfv-installers] Currently not all installers are supported.
### Fuel Installer
[featureusage:fuel-installer] OVSNFV project supplies a Fuel Plugin to upgrades Open vSwitch on an OPNFV installation to use user-space datapath.
As part of the upgrade the following changes are also made:
- change libvirt on compute node to 1.2.12
- change qemu on compute node to 2.2.1
- installs DPDK 2.0.0
- installs OVS 2.1 (specifically git tag 1e77bbe)
- removes existing OVS neutron plugin
- installs new OVS plugin as part of networking_ovs_dpdk OpenStack plugin version stable/kilo
- work around _set_device_mtu issue
### Limitations
[featureusage:limitations] This release should be considered experimental. In particular:
- performance will be addressed specifically in subsequent releases.
- OVS and other components are updated only on compute nodes.
### Bugs
[featureusage:bugs]
There may be issues assigning floating and public ip address to VMs.