# VSPERF Results
OPNFV
August 15, 2016
[index::doc]
# OPNFV Brahmaputra Scenarios
[scenario:opnfv-brahmaputra-scenarios][scenario::doc][scenario:vsperf-results] Available Tests and aspects of scenarios:
|L|L|
&
phy2phy_tput & PacketLossRatio for Phy2Phy
back2back & BackToBackFrames for Phy2Phy
phy2phy_tput_mod_vlan & PacketLossRatioFrameModification for Phy2Phy
phy2phy_cont & Phy2Phy blast vswitch at x% TX rate and measure throughput
pvp_cont & PVP blast vswitch at x% TX rate and measure throughput
pvvp_cont & PVVP blast vswitch at x% TX rate and measure throughput
phy2phy_scalability & Scalability0PacketLoss for Phy2Phy
pvp_tput & PacketLossRatio for PVP
pvp_back2back & BackToBackFrames for PVP
pvvp_tput & PacketLossRatio for PVVP
pvvp_back2back & BackToBackFrames for PVVP
phy2phy_cpu_load & CPU0PacketLoss for Phy2Phy
phy2phy_mem_load & Same as CPU0PacketLoss but using a memory intensive app
Supported deployment scenarios:
- Phy2Phy: Physical port -> vSwitch -> Physical port.
- PVP: Physical port -> vSwitch -> VNF -> vSwitch -> Physical port.
- PVVP: Physical port -> vSwitch -> VNF -> vSwitch -> VNF -> vSwitch -> Physical port.
Loopback applications in the Guest can be:
- DPDK testpmd.
- Linux Bridge.
- l2fwd.
Supported traffic generators:
- Ixia: IxOS and IxNet.
- Spirent.
- Dummy.
# OPNFV Brahmaputra Results
[results::doc][results:opnfv-brahmaputra-results] The vsperf CI jobs that were used to obtain the results can be found at https://wiki.opnfv.org/wiki/vsperf_results.
The following table maps the results in the test dashboard to the appropriate test case in the VSPERF Framework and specifies the metric the vertical/Y axis is plotting. Please note, the presence of dpdk within a test name signifies that the vswitch under test was OVS with DPDK, while its absence indicates that the vswitch under test was stock OVS.
|L|L|L|L|
& & &
tput_ovsdpdk & phy2phy_tput & Throughput (FPS) & N/A
tput_ovs & phy2phy_tput & Throughput (FPS) & N/A
b2b_ovsdpdk & back2back & Back-to-back value & N/A
b2b_ovs & back2back & Back-to-back value & N/A
tput_mod_vlan_ovs & phy2phy_tput_mod_vlan & Throughput (FPS) & N/A
tput_mod_vlan_ovsdpdk & phy2phy_tput_mod_vlan & Throughput (FPS) & N/A
scalability_ovs & phy2phy_scalability & Throughput (FPS) & N/A
scalability_ovsdpdk & phy2phy_scalability & Throughput (FPS) & N/A
pvp_tput_ovsdpdkuser & pvp_tput & Throughput (FPS) & vhost-user
pvp_tput_ovsvirtio & pvp_tput & Throughput (FPS) & virtio-net
pvp_b2b_ovsdpdkuser & pvp_back2back & Back-to-back value & vhost-user
pvp_b2b_ovsvirtio & pvp_back2back & Back-to-back value & virtio-net
pvvp_tput_ovsdpdkuser & pvvp_tput & Throughput (FPS) & vhost-user
pvvp_tput_ovsvirtio & pvvp_tput & Throughput (FPS) & virtio-net
pvvp_b2b_ovsdpdkuser & pvvp_back2back & Throughput (FPS) & vhost-user
pvvp_b2b_ovsvirtio & pvvp_back2back & Throughput (FPS) & virtio-net
The loopback application in the VNF used for PVP and PVVP scenarios was DPDK testpmd.